## Slide 1: EE307 Topic 1: Combinational logic review and Complementary MOSFET: CMOS
Complementary MOSFET: The first logic family (The first way to build gates from transistors)

## Slide 2: Overview of topic 1
SOP, POS, KMaps or something to come up with a gate representation of a truth table.
Gate based schematics are “block diagrams” of what a circuit looks like but not directly what goes into silicon. The “blocks” are the gate symbols.
Transistors, resistors, capacitors, inductors and memristors are what actually goes into silicon.
SO: You need to convert gates to transistors, resistors, inductors, and/or capacitors if you actually want to make a chip.

## Slide 3: Up-front comment
VHDL and Verilog don’t give you an optimized circuit
  Big 3: Speed, area and power
To optimize a circuit you must design at transistor level
Steps to get optimized transistor level circuit:
  Make truth table
  Find gate level circuit (SOP, POS, Kmaps etc)
  Design each gate in transistors
Step 1: Remember how to do SOP & POS

## Slide 4: REVIEW: SOP & POS Logic Gates – Combinational logic
Things to know about every basic gate
  Gate name
  Truth Table
  Symbol
  Notation (how it looks in an equation)

## Slide 5: Gate list:
  AND (mathematical partner: A x B)
  NOT/Inv (mathematical partner: -1 x A)
  OR (mathematical partner: A + B)
  XOR
  NAND
  NOR
  XNOR
  Buffer (mathematical partner: A)

## Slide 6: Symbol (AND) and notation
AND Gate
Notation
  A•B=OUT
A
B
OUT
Input |  | Output
A | B | OUT
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1

## Slide 7: Symbol (3-input AND) and notation
AND Gate
Notation
  A•B•C=OUT
A
B
OUT
Input |  |  | Output
A | B | C | OUT
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 0 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 0
1 | 1 | 1 | 1
C

## Slide 8: Symbol (XOR) and notation
XOR Gate (Exclusive OR gate)
Notation
  A ≠ B (For a two-input XOR)
Input |  | Output
A | B | OUT
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
A
B
OUT

## Slide 9: Symbol (Multi-input XOR)
XOR Gate (Exclusive OR
gate)
Notation
  A B C=OUT
  Meaning
  An odd number of ones
A
B
OUT
C
Input |  |  | Output
A | B | C | OUT
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 0
1 | 1 | 1 | 1

## Slide 10: XOR
XOR is associative in nature
A
B
C
D
E
F
OUT

## Slide 11: NAND gate : SOP
Change this table to a sentence:
(A • B) + (A • B) + (A • B)
= Output
Look at “1”s in Output column
and make sentence
Input |  | Output
A | B | TRUE?
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
Sum of products!!!!

## Slide 12: SOP
Find 1s in output column
Look at the inputs
Find an equation ANDing inputs that equals 1 for only those inputs – this is called a “Minterm”:
  “A product (ANDed) term in which each of the n variables appears once (in either its complemented or uncomplemented form) is called a minterm”.
Find all the 1s (outputs) and do steps 1-3 for each
OR all the minterms

## Slide 13: Product of sums example
Product of sums:
  Something like: (W+X)(Y+Z)
Look at “0”s. You want to find a sum for each row that gives the right output:
(A + B) (A + B)= Output
Input |  | Output
A | B | TRUE?
0 | 0 | 1
0 | 1 | 0
1 | 0 | 1
1 | 1 | 0
Make believe example. Nothing to do with NAND gate discussion

## Slide 14: POS
Find 0s in output column
Look at the inputs
Find an equation ORing inputs that equals 0 for only those inputs – this is called a “Maxterm”:
  “A sum term in which each of the n variables appears once (in either its complemented or uncomplemented form) is called a maxterm.”.
Find all the 0s (outputs) and do steps 1-3
AND all the maxterms

## Slide 15: Practice: Which is for SOP? Why?
Input |  |  | Output
A | B | C | OUT
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 0
1 | 1 | 1 | 1
Input |  |  | Output
A | B | C | OUT
0 | 0 | 0 | 1
0 | 0 | 1 | 1
0 | 1 | 0 | 1
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 0
1 | 1 | 1 | 0
SOP practice
POS practice

## Slide 16: Truth table
A | B | C | D | Z
0 | 0 | 0 | 0 | 1
0 | 0 | 0 | 1 | 0
0 | 0 | 1 | 0 | 1
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 0 | 0
0 | 1 | 0 | 1 | 1
0 | 1 | 1 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 0
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
1 | 0 | 1 | 1 | 1
1 | 1 | 0 | 0 | 0
1 | 1 | 0 | 1 | 1
1 | 1 | 1 | 0 | 1
1 | 1 | 1 | 1 | 1

## Slide 17: Kmap - SOP
CD\AB | 00 | 01 | 11 | 10
00 | 1 | 0 | 0 | 0
01 | 0 | 1 | 1 | 0
11 | 0 | 0 | 1 | 1
10 | 1 | 1 | 1 | 1

## Slide 18: Kmap - POS
CD\AB | 00 | 01 | 11 | 10
00 | 1 | 0 | 0 | 0
01 | 0 | 1 | 1 | 0
11 | 0 | 0 | 1 | 1
10 | 1 | 1 | 1 | 1

## Slide 19: Logic Families

## Slide 20: Logic families
Logic families
Static Logic
Adiabatic Logic
Current steering Logic
Clocked Logic
Ratioed Logic
Probability based Logic
And others….
Most popular, Rail to rail,
Robust,
Pretty fast,
Easy to design with…
Slow,
Low power
Newly popular,
Larger,
Not R2R
Can be:
Fast,
Low power, Can do non-inverting
Not used much now,
Power sucking,
Larger,
Complicated,
R2R
Pass transistor Logic
Can pass analog values too,
Simple,
Can be:
Small, Fast,
R2R,
Can do non-inverting
Not R2R,
Older family,
Many styles
New family, Usually R2R
CMOS

## Slide 21: Complementary MOSFET
Basics:
  “Static” logic family = low impedance path to VDD or GND to Vout
  Low Z path to VDD
  When you want Vout=High
  Low Z path to GND
  When you want Vout=Low
  Two circuits:
    Pull-up Network to pull Vout High
    Pull-down Network to pull Vout Low

## Slide 22: How to design PU and PD networks
We’ll start with a logic equation and make the circuits from there.
So all the combinational logic design steps through generating logic equations have come before we can do what we will do today.

## Slide 23: How CMOS works

## Slide 24: Transistors can be treated as switches
Bipolar Transistors
MOSFET* Transistors
*metal–oxide–semiconductor field-effect transistor
NMOS: (npn)
PMOS: (pnp)
C
C
B
B
E
E
E: Emitter
C: Collector
B: Base
S: Source
D: Drain
G: Gate
B: Bulk
D
G
S
S
G
D
pnp
npn
B
B

## Slide 25: Two types of switches: Type 1
Low
VLOW
VIN
Better for pulling values up
This node is pulled up to VDD
This node is pulled up to VDD
This node is pulled up to VDD
VDD
VDD
VDD
VIN
VIN
Conducts when Vin is low
PMOS
or
pnp

## Slide 26: Two types of switches: Type 2
High
VIN
Better for pulling values down
This node is pulled down to GND
GND
This node is pulled down to GND
This node is pulled down to GND
GND
Conducts when Vin is high
VIN
GND
VIN

## Slide 27: Why NMOS can’t pull voltage up
3.3V
3.3V
Say… 3.3V supply and VT=0.6V
VDS=VD – VS
We’ll raise VS and watch current
Voltage at VS only changes when current flows
We’ll hold VG and VD constant at 3.3V
VGS > VT for the transistor to conduct
IDS
VS
0 0.5 1.0 1.5 2.0 2.5 3.0 3.3
G
D
S

## Slide 28: Why PMOS can’t pull voltage down
Say… 3.5V supply and VT=0.8V
Vout=VDD
Then change Vin from VDD to GND
IDS
VSG
(Vout)
3.5 3.0 2.5 2.0 1.5 1.0 0.5
S
G
VDD

## Slide 29: Pull up and pull down networks
Pull-up network:
  pnp or PMOS
  (Because it has to be able to pull up Vout to VDD)
Pull-down network:
  npn or NMOS
  (Because it has to be able to pull down Vout to GND)

## Slide 30: First example: Inverter
First draw truth table:
First try at circuit: (Next slide)
INPUT | OUTPUT
Vin | Vout
0 | 1
1 | 0

## Slide 31: Inverter using switches
GND or
Logic 0
VSUP or
Logic 1
Low
High
VHIGH
VLOW
VIN
This node is pulled down to VLOW
This node is pulled up to VHIGH
Low
VHIGH
VLOW
VIN
High
OUT
A
A
A
Input | TRUE?
A | OUT
0 | 1
1 | 0

## Slide 32: Inverter using transistors
VSUP or
Logic 1
OUT
A
A
This node is pulled down to GND
This node is pulled down to GND
GND
VIN
GND
VIN
Low
High
GND or
Logic 0
A

## Slide 33: Inverter using transistors
VSUP or
Logic 1
OUT
A
A
Low
GND or
Logic 0
This node is pulled up to VDD
This node is pulled up to VDD
VDD
VDD
VIN
VIN
A

## Slide 34: MOSFETs vs BJTs for inverters
You can build an inverter using MOSFETs or BJTs BUT:
  MOSFETs are easier to automate and design with because Igate=0 whereas Ibase ≠0.
    Power
    Loading
  MOSFETs are easier to fabricate (= cheaper)
  MOSFETs give more options for low voltage design.
We’ll use CMOS=MOSFETs

## Slide 35: NAND gate Built with Switches
(A • B) + (A • B) + (A • B) = Output
Input |  | Output
A | B | TRUE?
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
1
1
B
A
GND
0
0
B
A
VSUP
VSUP

## Slide 36: Rules for implementing (complex) logic equation in transistors (CMOS) (1/5)
Step 1: Try to get an equation with a bar all the way across the equation
  Good:
    The bar covers the entire equation
  Not good (1):
    The bar isn’t continuous
  Not good (2):
    Though there’s a bar across entire equation, internally, there’s a bar across more than one input

## Slide 37: Example….
A | B | C | Out
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 0
C\AB | 00 | 01 | 11 | 10
0 | 0 | 1 | 1 | 1
1 | 0 | 0 | 0 | 0

## Slide 38: Example: Getting single bar across entire equation
Let’s take this equation:
First negate entire equation twice:
Keep top bar but “DeMorgan” inside:
Not done because of internal bar across more than one input. “DeMorgan” again:

## Slide 39: What we have at this point
You have an equation with a bar over the whole thing:
You know that the order of operations say you do the AND before the OR.
You know the inputs to your circuit:
This means that A and B must be inverted (put through an inverter) before they are used by this circuit. C is not inverted so OK as is.

## Slide 40: Black box picture of circuit
Final equation and its inputs:

## Slide 41
If the equation is:
What is the converted equation?
What are the inputs?
  .
Practice:

## Slide 42: Rules for implementing (complex) logic equation in transistors (CMOS) (2/5)
Creating pull-down network:
  Use NMOS (conduct-on-high switches)
  Take equation under bar.
    So if equation is:
    The equation you want is: (Just remove top bar)
  >> Continued on next slide

## Slide 43: Rules for implementing (complex) logic equation in transistors (CMOS) (3/5)
Creating pull-down network:
  In pulldown network, ANDs are in series and ORs are in parallel. (Assume inputs are given even if they are negated)
    are ANDed so they go in series:
    so it goes in parallel:

## Slide 44: Checking pulldown network (1/2)
The equation we are trying to implement probably came from a truth table but we started with an equation. We need the truth table to be able to check our circuit. Here’s the original equation:
A | B | C | Out
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 0

## Slide 45: Checking pulldown network (2/2)
This must pulldown for Vout=0 and open circuit for Vout=1.
A | B | C | Out
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 0

## Slide 46: Rules for implementing (complex) logic equation in transistors (CMOS) (4/5)
Creating pull-up network:
  Use PMOS (conduct-on-low switches)
  Anything that was in parallel in the pulldown network is now in series.
  Anything that was in series in the pulldown network is now in parallel.

## Slide 47: Checking pull-up network
This must pull up for Vout=1 and open circuit for Vout=0.
A | B | C | Out
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 0

## Slide 48: Summary so far
Find equation from truth table
KMaps are good because simpler equations are simpler to implement
Manipulate equation so it has a bar over entire equation
Create pulldown network from equation under bar
  AND is series
  OR is parallel
  Open circuit when output is high
  Short circuit when output is low
Create pullup network
  AND is parallel
  OR is series
  Open circuit when output is high
  Short circuit when output is low

## Slide 49: Rules for implementing (complex) logic equation in transistors (CMOS) (5/5)
Final design:

## Slide 50: Final things to note
We’ve ignored details:
  Larger transistors = More current = faster transitions
  Increase in current = Increase in power
  Region of operation = Affects current
  Larger transistors = More capacitance = slower transitions
  Stacking transistors increases delay exponentially
We’ll continue to practice design but next we’ll delve into these details for the next week

## Slide 51: More notes on CMOS
Transistors are naturally inverting. They like NAND, NOR and inverters.
If you want to implement a non-inverting circuit like an AND or OR, you need to implement a NAND or NOR and then put the NAND or NOR output through an inverter or use inverted inputs.
The pull-up network can be found from the original equation but inputs must be inverted. If you are interested in creating the pull-up network this way, figure out the rules yourself.

## Slide 52: Practice
Implement a half-adder summing circuit
Implement a half-adder carry circuit
XNOR

## Slide 53: Answers to practice problems
Problem 1:  On homework so all yours
Problem 2: AND
Change the equation to get a bar over the entire equation:
That tells you that the inputs to the PU and PD networks are and .
The logic for the PD network is:

## Slide 54: Answers to practice problems
Problem 2 continued:
PD network for . It’s an OR so the transistors go in parallel (AND is in series, OR is in parallel):
PU network puts anything that was in parallel in the PD network in series and anything that was in series in parallel:

## Slide 55: Answers to practice problems
Problem 2 continued:
Complete circuit
Note that the inputs are inverted. That means you need some inverters before this circuit. NAND and NOR are inverting and their inputs don’t need to be inverted. Non-inverting circuits will need extra circuitry around them. Either an inverter on the output or inverters on the inputs. Naturally inverting circuits like NAND, NOR and INV won’t.

## Slide 56: Answers to practice problems
Problem 3: Implement a half-adder summing circuit  On homework…
Problem 4: Implement a half-adder carry circuit  On homework…
Problem 5: XNOR
Already has a bar across the top so it’s in the form we need to design PD and PU networks.

## Slide 57: Answers to practice problems
Problem 5 continued:

## Slide 58: Practice Problem 6:
Pulldown network
  From the equation, look for ANDs and ORs:
    ORs translate into parallel transistors
    ANDs translate into serial transistors

## Slide 59: Practice (CMOS)
Pullup network

## Slide 60: Practice (CMOS)
Step 6: Put PU network together with PD network:

## Slide 61: EXTRA SLIDES

## Slide 62: AND gate Built with Switches
(A • B) + (A • B) + (A • B) = Output
Input |  | Output
A | B | TRUE?
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
0
1
VOUT
VSUP
GND
1
1
B
A
GND
0
0
B
A
VSUP
VSUP

## Slide 63: XNOR gate Built with Switches
Input |  | Output
A | B | OUT
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
0
A
VSUP
0
B
0
A
VSUP
0
B
1
1
B
A
1
1
B
A
OUT