## Slide 1: EE307 Topic 2: Complementary MOSFET inverter details
Part 1:
Inverter static and dynamic metrics

## Slide 2: Practice
Find complex gate circuits for these equations

## Slide 3: Overview of topic 2
You should now feel OK designing complementary MOSFET complex circuits.
Now we’ll see:
  DC and dynamic characteristics
  What a good digital circuit looks like
  How to put numbers to describe a digital circuit (metrics)
  Find speed and power of a digital circuit
We’ll use the simplest complementary MOSFET circuit in this analysis: an inverter.

## Slide 4: DC Characteristics

## Slide 5: DC means no time involved
Simulation types for DC metrics:
  DC bias point (.op)
    DC bias point (.op) puts DC value on input and, after everything settles tells you what the node voltages are and what branch currents are for that SINGLE DC input
  DC sweep:
    DC sweep puts DC value on input and, after everything settles tells you what the node voltages are and what branch currents are
    Does this for a set of inputs and them connects the dots
    NO TIME INVOLVED
    Capacitors open circuited
    Inductors shorted

## Slide 6: Vocabulary for DC description/metrics of (digital) circuits

## Slide 7: Language of digital circuits
Terms used to describe performance (static=DC)
  Vm : Vin=Vout
  Vmax, Vmin , VOH, VOL, VIH, VIL, NMH, NML
Vm

## Slide 8: NMH and NML tell you:
NM = Noise margin
NMH = Noise margin high
NML = Noise margin low
And tell you:
  How robust a digital circuit is to noise
  How much noise you can have on a circuit and still get the right answer

## Slide 9: Noise types
GND/Supply noise:
  Current rushing on and off of GND and power plane
Signal noise:
  Capacitive coupling
  IR drop
Intrinsic noise
  Current doesn't flow smoothly
Many digital logic families cause A LOT of GND and supply noise. They need to be robust.

## Slide 10: Bypass Capacitors (2) Noisy signals

## Slide 11: Inductive supply noise
GND or VDD/VCC has a bunch of charge removed (added)
To get GND or VDD/VCC back to where it should be there is a rush of charge on to (off of) GND/VDD/VCC
The current induces a magnetic field = induction
Even after GND/VDD/VCC reaches its correct value, the current doesn’t stop
= More bouncing…

## Slide 12: Where does noise on the signal line come from?
vin
D
~
vin
+
--
1V
Capacitive coupling from nearby wire or E&M transmision (cell phone, computer, etc)
60Hz noise and high-frequency noise common

## Slide 13: Where does supply (VDD, VCC, GND) noise come from?
Digital (synchronous) systems suck electrons off GND each time the clock ticks
  Removing negative charge makes GND a little more positive until electrons can be restored
  At high frequencies, inductance can be a factor and the rush of electrons to restore the electrons on GND plane can cause overshoot and temporarily make GND more negative than it should be
Digital (synchronous) systems dump electrons onto VDD/VCC each time the clock ticks
  Same effects as above
Same causes as signal noise

## Slide 14: Intrinsic Noise
Shot noise: Associated with DC current flow. Present in diodes, BJTs and MOSFETs. The random pace at which electrons jump across depletion region.
Thermal noise: Thermal motion of electrons. Directly proportional to T. Nothing to do with current.
Flicker (1/f) noise: Traps caused by contamination of silicon and crystal defects.
Burst (popcorn) noise: Source unknown – might be from heavy metal ion contamination.
Avalanche noise: Avalanche breakdown in pn junction. Holes and electron pairs acquire sufficient energy to create pairs upon colliding with silicon atoms.

## Slide 15: NMH, NML: Noise margins
VILmin VIL VIH VIHmax
VOLmin VOL VOH VOHmax
Inverter 1
Inverter 2
2x
2x
Noise margin equations:
Noise margin (low):
NML=VIL - VOLmin
Noise margin (high):
NMH=VOHmax - VIH
VOHmax
VOLmax
V’

## Slide 16: NOTE: Definition of NMH, NML vary
Different books and websites define NMH and NML differently.
Gopalan uses different definition.

## Slide 17: NMH, NML: Noise margins (1)
Inverter 1
Inverter 2
Inverter 1
Inverter 2
VIH
VIL
VOHmax
VOLmin
2x
2x
Noise margin equations:
Noise margin (low):
NML=VIL - VOLmin
Noise margin (high):
NMH=VOHmax - VIH
VOHmax
VOLmax

## Slide 18: Summary of digital circuit metrics

## Slide 19: Summary of digital circuit metrics
Terms used to describe performance (static=DC)
  Vm : Vin=Vout
  Vmax, Vmin , VOH, VOL, VIH, VIL, NMH, NML
Vm

## Slide 20: ON or OFF

## Slide 21: Analysis 1/2: What’s on?
Vout Pulled down
Vout Pulled up
ON/OFF graph:
  Vin on X-axis
  ON/OFF on Y-axis
Example 1:
(Add line for M1 and M2 )
  VTN = 0.5V, VTP = -0.6V, VDD = 3.3V
Vin
ON
OFF
0 0.5 1.0 1.5 2.0 2.5 3.0 3.5
Short circuit current
Vin | Vout
0 | 1
1 | 0
Vin | VGSN | VGSP | M1 | M2
0 | 0 | -3.3 | X | O
0.2 | 0.2 | -3.1 | X | O
0.4 | 0.4 | -2.9 | X | O
0.5 | 0.5 | -2.8 | o | O
0.6 | 0.6 | -2.7 | O | O
1.5 | 1.5 | -1.8 | O | O
2.1 | 2.1 | -1.2 | O | O
2.7 | 2.7 | -0.6 | O | o
3.0 | 3.0 | -0.3 | O | X
3.3 | 3.3 | -0.0 | O | X
NOTE: VDD > VTN + |VTP|
What’s width of the SS section?
VDD – (VTN + |VTP|)=Width

## Slide 22: Analysis 2/2: What’s on?
ON/OFF graph:
  Vin on X-axis
  ON/OFF on Y-axis
Example 1: (Add line for M1 and M2 )
  VTN = 0.5V, VTP = -0.6V, VDD = 1V
Vout Pulled down
Vout Pulled up
Vin
ON
OFF
0 0.2 0.4 0.6 0.8 1.0 1.2
Open circuit
What happens in that center section?
(VTN + |VTP|)-VDD =Width

## Slide 23: Regions of operation

## Slide 24: Regions of operation 1/5: Transfer characteristics
Graph that has Vin on X-axis and Vout on Y-axis.
VTN = 0.75V, VTP = -0.8V, VDD = 3.3V
Vin
0 0.5 1.0 1.5 2.0 2.5 3.0 3.5
Vout
0 0.5 1.0 1.5 2.0 2.5 3.0 3.5
SP
GN
SN
GP

## Slide 25
Graph that has Vin on X-axis and Vout on Y-axis.
VTN = 0.75V, VTP = -0.8V, VDD = 3.3V
Vout Pulled down.
M1 on
Vout Pulled up.
M2 on
Vin
0 0.5 1.0 1.5 2.0 2.5 3.0 3.5
Short circuit current
Vout
0 0.5 1.0 1.5 2.0 2.5 3.0 3.5
Regions of operation 2/5: Transfer characteristics

## Slide 26: (Voltage) Transfer characteristic: VTC
A description of what happens to Vout when Vin is changed
Has nothing to do with time
“When you give the circuit a Vin value, what is the Vout value after the circuit has been given time to settle? Draw that point. Then give it a different Vin value and find Vout. Draw that point. Repeat a million time then connect all the points into a curve. That’s a VTC”
DC sweep simulation
DC sweep simulation
Has nothing to do with time

## Slide 27: Regions of operation 3/5: Transfer characteristics M1
Graph that has Vin on X-axis and Vout on Y-axis.
VTN = 0.75V, VTP = -0.8V, VDD = 3.3V
0 0.5 1.0 1.5 2.0 2.5 3.0 3.5
Vout
(VDS)
0 0.5 1.0 1.5 2.0 2.5 3.0 3.5
VGSN < 0.75
Vout Pulled up.
M2 ON
Short circuit current
Vout Pulled down.
M1 on
M1 in cutoff
VGSN > 0.75
VGSN – VTN = Vin – 0.75V
VDS = Vout
Vin – 0.75V < Vout
Vin < Vout + 0.75V
VGSN > 0.75
Vin – 0.75V > Vout
M1 in saturation
M1 in linear
M1 in linear
Vm
Vin=Vout
VGS-VT=VDS
Vin-VT=Vout
Vin
(VGS)
VTN

## Slide 28: Regions of operation 4/5: Transfer characteristics M2
Graph that has Vin on X-axis and Vout on Y-axis.
VTN = 0.75V, VTP = -0.8V, VDD = 3.3V
Vin
0 0.5 1.0 1.5 2.0 2.5 3.0 3.5
Vout
0 0.5 1.0 1.5 2.0 2.5 3.0 3.5
Vout Pulled up.
M2 ON
Short circuit current
M2 in cutoff
M2 in linear
|VGSP| - |VTP| = |VDSP|
VDD - Vin – 0.8 = VDD – Vout
Vin-0.8=Vout
Vin=Vout+0.8
M2 in linear
Vout Pulled down.
M1 on
M2 in saturation
VTP

## Slide 29: Regions of operation 5/5: Transfer characteristics M2
Graph that has Vin on X-axis and Vout on Y-axis.
VTN = 0.75V, VTP = -0.8V, VDD = 3.3V
Vin
0 0.5 1.0 1.5 2.0 2.5 3.0 3.5
Vout
0 0.5 1.0 1.5 2.0 2.5 3.0 3.5
Vout Pulled up.
M2 ON
Short circuit current
Vout Pulled down.
M1 on
M1 in cutoff
M1 in saturation
M1 in linear
M2 in cutoff
M2 in saturation
M2 in linear
Short circuit current
Worst short circuit current
When are transistors on?

## Slide 30: Looks bad but it’s not as bad as it looks
0.0 0.5 1.0 1.5 2.0 2.5 3.0 3.5

## Slide 31: Shape of graph using load lines

## Slide 32: Looking at inverter as voltage divider
If Vin is small, M1 won’t be
conducting much.
If Vin is small, M2 will be
conducting a lot.
That equates to:
  Vout is large or small?
What about if Vin is large?
  Vout is large or small?

## Slide 33: Analysis technique: Load line
Divide circuit into two parts and come up with voltages and currents that make them both happy.
DC solution
Let’s do a voltage divider:

## Slide 34: Steps for load line analysis Example 1
Cut it in half
Graph each half separately
Find where both are satisfied
VDD/Rtop
VDD/Rbottom

## Slide 35: Steps for load line analysis Example 1
Cut it in half
Graph each half separately
Find where both are satisfied
VDD/Rtop
VDD/Rbottom
Itop
Ibottom
Only place where Itop equals Ibottom
Operating point
Vout
I

## Slide 36: New logic family
RTL: Resistor-transistor logic family
  Pull up network is a resistor
  Old logic family
  Voutmax? VDD
  Voutmin? VDD - [ IDS(VGS=VDD) x Rtop]
  Which NM suffers? (Vin) NML
  What else is wrong with this logic family?
  Power  When Vout is low, current will be flowing continuously
  Resistors are large

## Slide 37: Steps for load line analysis Example 2
Cut it in half
Graph each half separately
Find where both are satisfied
VDD/Rtop
Only place where Itop equals Ibottom
Operating point

## Slide 38: Steps for load line analysis Example 2
Cut it in half
Graph each half separately
Find where both are satisfied
VDD/Rtop
Only place where Itop equals Ibottom
Operating point
Itop
Ibottom
Vout
I

## Slide 39: Inverter – More detail
NMOS
  Cutoff (VGS < VTN)
  Linear, Ohmic, resistive
  (VGS > VTN, VDS < VGS-VT)
  Active, saturation, pinch-off
  (VGS > VTN, VDS > VGS-VT)
NOTE: IDS > 0
VGS > 0
VT > 0
VDS > 0
kn’ > 0
Case 1: Vin=3.3V
Case 2: Vin=GND
Case 3: Vin=VTN
Case 4: Vin=VDD-|VTP|
Case 5: Vin=Vsup/2
Notes: Shichman–Hodges model – that’s what this equation is called

## Slide 40: Looks bad but it’s not as bad as it looks
Short circuit current looks bad… But if you are only in the middle region for a short period of time, it doesn’t hurt too much.
If λ is small and IDS changes, the circuit will quickly switch Vout from high to low or low to high.
Explain this to your neighbor

## Slide 41: Finding points on graph w/ math (1/8)
Vin < VTN
M1 is in cutoff.
The same current must be going through both M1 and M2.
So M2 has to be conducting 0A.
But its VGS=VDD so M2 on.
Region of operation? Linear
VGS is constant and VDS is
changing so what graph is
appropriate?
And where is the PMOS operating?

## Slide 42: Need to figure out right Vout for equal current through M1 and M2
Cut it in half
Graph each half separately
Find where both are satisfied
Only place where Itop equals Ibottom
Operating point
Vout
I
VG

## Slide 43: VTC
Vin=0V, Vout=10V
Vin=1.5V, Vout=10V
Vin=2V, Vout=9.98V
Vin=2.5V, Vout=9.78V
Vin=3V, Vout=9.748V
Vin=3.5V, Vout=9.51V
Vin=4V, Vout=9.12V
Vin=4.5V, Vout=8.35V
Vin=4.6V, Vout=8.05V
Vin=4.7V, Vout=7.51V
Vin=4.8V, Vout=5.88V
Vin=4.9V, Vout=3.79V
Vin=5V, Vout=2.32V
Vin=5.5V, Vout=0.97V
Vin=6V, Vout=0.56V
Vin=6.5V, Vout=0.32V
Vin=7V, Vout=0.10V
Vin=7.5V, Vout=0.06V
Vin=8V, Vout=0.01V
Vin=8.5V, Vout=0V
Vin=10V, Vout=0V

## Slide 44: Graphing….
Vin=0V, Vout=10V
Vin=1.5V, Vout=10V
Vin=2V, Vout=9.98V
Vin=2.5V, Vout=9.78V
Vin=3V, Vout=9.748V
Vin=3.5V, Vout=9.51V
Vin=4V, Vout=9.12V
Vin=4.5V, Vout=8.35V
Vin=4.6V, Vout=8.05V
Vin=4.7V, Vout=7.51V
Vin=4.8V, Vout=5.88V
Vin=4.9V, Vout=3.79V
Vin=5V, Vout=2.32V
Vin=5.5V, Vout=0.97V
Vin=6V, Vout=0.56V
Vin=6.5V, Vout=0.32V
Vin=7V, Vout=0.10V
Vin=7.5V, Vout=0.06V
Vin=8V, Vout=0.01V
Vin=8.5V, Vout=0V
Vin=9V, Vout=0V
Vin=10V, Vout=0V
Vin
Vout
0 1 2 3 4 5 6 7 8 9 10
0 1 2 3 4 5 6 7 8 9 10

## Slide 45: Circuits used

## Slide 46: Just a reminder….
The VTC is for finding the DC characteristics and those include VIL, VIH, VOL, VOH, Vm, NMH and NML
Next we’ll look at the time dependent stuff: Delays (=speed of your circuit)
We’ll stick with inverters for the rest of this topic but, in the next topic, we’ll look at how you’d find the delay for a complex CMOS gate.

## Slide 47: Language of digital circuits
Terms used to describe performance (static=DC)
  Vm : Vin=Vout
  Vmax, Vmin , VOH, VOL, VIH, VIL, NMH, NML
Vm

## Slide 48: Vm: Currents equal and in the active region

## Slide 49: Vm we’ll use
I’ll expect you to know how to find Vm but…
We’ll use: Vm = (Vomax – Vomin)/2

## Slide 50: NOTE: Definition of NMH, NML vary
Different books and websites define NMH and NML differently.
Gopalan uses different definition.

## Slide 51: Techniques to find VIL, VIH, VOL & VOH (m = -1 slope points)
Understanding what they mean is most important BUT, if you did want to do the math…..
Techniques
  Reading it off a graph
  Find slope at Vm and extrapolate
  Load line knowing that the same current goes through top and bottom and then do implicit differentiation

## Slide 52: Find slope at Vm and extrapolate
Vomax
Vomin
m = -1
m = -1
Slope @ Vm = -g
Vm @ Vin=Vout=VDD/2
or, more correctly:
Vm = (Vomax-Vomin)/2
Y=mx+b  Vout(Vin) = -g·Vin+b
To find “b”, set Vin=Vout=Vm:
Vm = -g·Vm + b  b = Vm(1+g)
To find Vins:
Vout = -g·Vin + Vm(1+g)
Vomax = -g·Vin1 + Vm(1+g)
Vomin = -g·Vin2 + Vm(1+g)

## Slide 53: Finding “g”
EE308 topic
Where IDS is the current at Vin(VGS)=Vm
I’ll show you math if you’d like. Take EE308 to see where this came from.

## Slide 54: Implicit Differentiation (1/)
Tough to separate Y from X
Need to use “Implicit Differentiation”
Treat Y as a function of X
Product Rule:
Power Chain Rule:

## Slide 55: Implicit Differentiation (1/)
Look at single term:
Derivative with respect to X:
Doing the entire equation you get:

## Slide 56: Implicit Differentiation (1/)
Look at single term:
Derivative with respect to X:
Doing the entire equation you get:

## Slide 57: Implicit Differentiation to find -1 slope point (Slope=dY/dX=dVout/dVin=dVDS/dVGS) VOH, VIL
Taking the derivative with respect to VGS:
Still have both VDS and VGS in equation

## Slide 58: Final word on VIL, VIH, VOL and VOH
Know how to use the slope to get Vin for VIH and VOH (method 2)
Also know how to read off the graph (method 1 and what you would use in experimental situations)
Method 3 is for reference

## Slide 59: Slope = Gain (Digital/EE307)
The operating region for EE307 and EE308
Vout Pulled down.
M1 on
Vout Pulled up.
M2 on
Vin
0 0.5 1.0 1.5 2.0 2.5 3.0 3.5
Short circuit current
Vout
0 0.5 1.0 1.5 2.0 2.5 3.0 3.5
Clearly high! No doubt it’s a logic ‘1’
Clearly low! No doubt it’s a logic ‘0’
Not as clear whether it’s a ‘1’ or a ‘0’
Good digital region
Good digital region
Bad digital region

## Slide 60: Slope = Gain (Analog/EE308)
The operating region for EE307 and EE308
Vout Pulled down.
M1 on
Vout Pulled up.
M2 on
Vin
0 0.5 1.0 1.5 2.0 2.5 3.0 3.5
Short circuit current
Vout
0 0.5 1.0 1.5 2.0 2.5 3.0 3.5
Change Vin: Vout doesn’t change
Change Vin: Vout doesn’t change
Change Vin: Vout does change
Bad analog region
Bad analog region
Good analog region

## Slide 61: Slope < 1: How much does Vout change?
What’s the slope?: 0.5V/2V=1/4
VTC
Transient Response

## Slide 62: Slope < 1: How much does Vout change?
What’s the VTC slope?: 0.5V/2V=1/4
What’s the input slope?:
What’s the output slope?:
VTC
Transient Response

## Slide 63: Slope < 1: How much does Vout change?
What’s the VTC slope?: 6V/2V=3
What’s the input slope?:
What’s the output slope?:
VTC
Transient Response
6V
6V
3V

## Slide 64: Simpler version
INPUT (m=1/2)
INPUT (m=1/2)




VTC (m=1/4)
VTC (m=1.5)
OUTPUT (m=1/8)
OUTPUT (m=3/4)

## Slide 65: Even simpler version
m=X
m=2∙X
m=X
m=X/2

## Slide 66: Another way to divide up graph
Before: Divided up graph by transistor region of operation
Now: Divide up graph by regenerative and non-regenerative regions
Vin
0 0.5 1.0 1.5 2.0 2.5 3.0 3.5
Vout
0 0.5 1.0 1.5 2.0 2.5 3.0 3.5
|Slope| > 1
Slope = -1
|Slope| < 1
Slope = -1
Slope < -1

## Slide 67: Regenerative circuit
If the slope of (most of) the transition region has a |slope| > 1 then the circuit is called regenerative.
If the slope of (most of) the transition region has a |slope| < 1 then the circuit is called non-regenerative.

## Slide 68: Regeneration – Regenerative circuits
With good transitions, the circuit will only be in the short circuit region for a short time.

## Slide 69: Dynamic metrics: Delay

## Slide 70: Language of digital circuits (2)
Terms used to describe performance (dynamic)
  tPHL, tPLH
  tR, tF
New terms
  Fan-in = # of inputs
  Fan-out = # of circuits being driven by output of circuit

## Slide 71: Delay is how long it takes to charge capacitance through transistor
The capacitance is the capacitance from the transistors and the wires
The capacitances get charged up (and discharges) by current through a transistor
Transistor is like an “R”
C is “C”
Vin
+
--
R
VOUT
C from transistors and wires
R-like behavior from transistors not giving infinite current

## Slide 72: What we’ll look at
How to find “R”
  Not a real resistor
  Current through transistor, voltage across transistor
    Not quite that simple….
How to find “C”
  Sum of capacitances on transistor
  Plus sum of capacitances on wire

## Slide 73: Delay equation = RC
The capacitance is the capacitance from the transistors and the wires
The capacitances get charged up (and discharges) by current through a transistor
Transistor is like an “R”
C is “C”
Vin
+
--
R
VOUT

## Slide 74: Delay equation = RC
RC time constant
Vin
+
--
R
VOUT

## Slide 75: Delay calculation: tp Low to high
Assume: Vmax=VDD, Vm=VDD/2 and that Vin switches instantaneously.

## Slide 76: Delay calculation: tp High to low
Assume: Vmax=VDD, Vm=VDD/2 and that Vin switches instantaneously.

## Slide 77: Moral of the story
R of a node times C of a node times 0.69 = tp
Next: How to find R and C

## Slide 78: Resistance

## Slide 79: R for tpHL calculation
Not actual resistor  Perceived resistance:
  Voltage across transistor
  Current through transistor

## Slide 80: Calculate R: (Technique 1)
Take average over range by integration

## Slide 81: Calculate R: (Technique 2)
Take average of ends of range

## Slide 82: Calculate R: (Technique 3)
Randomly pick a point near the middle of the region:

## Slide 83: Transient Response
tpHL = 0.69 CL Reqn
tpLH = 0.69 CL Reqp
tp = 0.69 CL (Reqn+Reqp)/2
?
tpLH
tpHL

## Slide 84: Calculating R and C of wires

## Slide 85: Wire R calculation
Equation:
L=Length of wire
W=Width of wire
Example: N+ L=10μm, W=1μm

## Slide 86: Wire C calculation
 C = Area x C per unit area
C per unit area:
Example: C between M1 and M2=116aF/µm2
So 1µm x 1µm area would have 116aF of C

## Slide 87: S & D Resistance
Generally
  20-100
Silicidation
  Coat S and D with titanium or tungsten
  1-4
RS
RD

## Slide 88: Capacitance of transistors

## Slide 89: Example: Intel early chip

## Slide 90: Capacitance
Diffusion
Capacitance
Diffusion
Capacitance
Channel (Gate)
Capacitance
Physical
(Overlap)
Capacitance
Physical
(Overlap)
Capacitance
CSB
CDB
CGDOV
CGSOV
CGC
(Different for different regions of operation)
Notes: Remember to explain field effect

## Slide 91: Three sources of capacitance in MOSFETs
Basic MOS structure
  Two conductors separated by insulator
Channel charge
  Channel (either charge or substrate) forms second plate
Depletion region
  PN junctions

## Slide 92: Basic MOS Structure Capacitance CGS = CGS0W, CGD = CGD0W
t
ox
n
+
n
+
Cross section
L
Gate oxide
x
d
x
d
L
d
Polysilicon gate
Top view
Gate-bulk
overlap
Source
n
+
Drain
n
+
W
Always Exists
(Included in gate capacitance)

## Slide 93: Channel Capacitance CGB, CGS, CGD =Gate
Cut-off
Resistive
Saturation
Plus overlap capacitance
C to substrate
C to charge
C to charge but that’s only 2/3 of channel
Cutoff
Linear
Active

## Slide 94: Depletion Region Capacitance “Diffusion” Capacitance
Bottom
Side wall
Side wall
Channel
Source
N
D
Channel-stop implant
N
A
1
Substrate
N
A
W
x
j
L
S
Cdiff
= CBottom
CBottom
Bulk
+ CSW
CSW
CSW
CSW
= Cj x Area + Cjsw x PERIMETER

## Slide 95: (Single) MOSFET capacitance calculation
Region of operation: Gate C differs
Find where we’re sitting: You’ll be looking from the gate, drain or source. Figure out which one.
We’ll do all three… Looking into the gate first.

## Slide 96: (Single) MOSFET gate capacitance
Three components:
  Channel capacitance:
  Basic MOS structure:
  Depletion regions:

## Slide 97: SPICE NMOS Model
.MODEL N1 NMOS LEVEL = 14
+VERSION = 4.6.0 BINUNIT = 1 PARAMCHK= 1 MOBMOD = 0
+CAPMOD = 2 IGCMOD = 1 IGBMOD = 1 GEOMOD = 1
+DIOMOD = 1 RDSMOD = 0 RBODYMOD= 0 RGATEMOD= 1
+PERMOD = 1 ACNQSMOD= 0 TRNQSMOD= 0 TEMPMOD = 0
+TNOM = 27 TOXE = 1.8E-009 TOXP = 10E-010 TOXM = 1.8E-009
+DTOX = 8E-10 EPSROX = 3.9 WINT = 5E-009 LINT = 1E-009
+LL = 0 WL = 0 LLN = 1 WLN = 1 +LW = 0 WW = 0 LWN = 1 WWN = 1
+LWL = 0 WWL = 0 XPART = 0 TOXREF = 1.4E-009
+SAREF = 5E-6 SBREF = 5E-6 WLOD = 2E-6 KU0 = -4E-6
+KVSAT = 0.2 KVTH0 = -2E-8 TKU0 = 0.0 LLODKU0 = 1.1
+WLODKU0 = 1.1 LLODVTH = 1.0 WLODVTH = 1.0 LKU0 = 1E-6
+WKU0 = 1E-6 PKU0 = 0.0 LKVTH0 = 1.1E-6 WKVTH0 = 1.1E-6
+PKVTH0 = 0.0 STK2 = 0.0 LODK2 = 1.0 STETA0 = 0.0 +LODETA0 = 1.0
+LAMBDA = 4E-10 VSAT = 1.1E+005 +VTL = 2.0E5 XN = 6.0 LC = 5E-9
+RNOIA = 0.577 RNOIB = 0.37 +LINTNOI = 1E-009
+TVOFF = 0.0 TVFBSDOFF = 0.0
+VTH0 = 0.25 +K1 = 0.35 K2 = 0.05 K3 = 0
+K3B = 0 W0 = 2.5E-006 DVT0 = 1.8 DVT1 = 0.52
+DVT2 = -0.032 DVT0W = 0 DVT1W = 0 DVT2W = 0
+DSUB = 2 MINV = 0.05 VOFFL = 0 DVTP0 = 1E-007
+DVTP1 = 0.05 LPE0 = 5.75E-008 LPEB = 2.3E-010 XJ = 2E-008
+NGATE = 5E+020 NDEP = 2.8E+018 NSD = 1E+020 PHIN = 0
+CDSC = 0.0002 CDSCB = 0 CDSCD = 0 CIT = 0
+VOFF = -0.15 NFACTOR = 1.2 ETA0 = 0.05 ETAB = 0
+UC = -3E-011 +VFB = -0.55 U0 = 0.032 UA = 5.0E-011 UB = 3.5E-018
+A0 = 2 AGS = 1E-020 +A1 = 0 A2 = 1 B0 = -1E-020 B1 = 0
+KETA = 0.04 DWG = 0 DWB = 0 PCLM = 0.08
+PDIBLC1 = 0.028 PDIBLC2 = 0.022 PDIBLCB = -0.005 DROUT = 0.45
+PVAG = 1E-020 DELTA = 0.01 PSCBE1 = 8.14E+008 PSCBE2 = 5E-008
+FPROUT = 0.2 PDITS = 0.2 PDITSD = 0.23 PDITSL = 2.3E+006
+RSH = 0 RDSW = 50 RSW = 50 RDW = 50
+RDSWMIN = 0 RDWMIN = 0 RSWMIN = 0 PRWG = 0
+PRWB = 6.8E-011 WR = 1 ALPHA0 = 0.074 ALPHA1 = 0.005
+BETA0 = 30 AGIDL = 0.0001 BGIDL = 2.1E+009 CGIDL =
+EGIDL = 0.8 AGISL = 0.0002 BGISL = 2.1E+009 CGISL = 0.0002
+EGISL = 0.8 +AIGBACC = 0.012 BIGBACC = 0.0028 CIGBACC = 0.002
+NIGBACC = 1 AIGBINV = 0.014 BIGBINV = 0.004 CIGBINV = 0.004
+EIGBINV = 1.1 NIGBINV = 3 AIGC = 0.012 BIGC = 0.0028
+CIGC = 0.002 AIGS = 0.012 BIGS = 0.0028 CIGS = 0.002
+NIGC = 1 POXEDGE = 1 PIGCD = 1 NTOX = 1
+AIGD = 0.01 BIGD = 0.003 CIGD = 0.0015 +XRCRG1 = 12 XRCRG2 = 5
+CGSO = 6.238E-010 CGDO = 6.238E-010 CGBO = 2.56E-011 CGDL = 2.495E-10
+CGSL = 2.495E-10 CKAPPAS = 0.03 CKAPPAD = 0.03 ACDE = 1
+MOIN = 15 NOFF = 0.9 VOFFCV = 0.02
+KT1 = -0.37 KT1L = 0.0 KT2 = -0.042 UTE = -1.5
+UA1 = 1E-009 UB1 = -3.5E-019 UC1 = 0 PRT = 0 +AT = 53000
+FNOIMOD = 1 TNOIMOD = 0
+JSS = 0.0001 JSWS = 1E-011 JSWGS = 1E-010 NJS = 1
+IJTHSFWD= 0.01 IJTHSREV= 0.001 BVS = 10 XJBVS = 1
+JSD = 0.0001 JSWD = 1E-011 JSWGD = 1E-010 NJD = 1
+IJTHDFWD= 0.01 IJTHDREV= 0.001 BVD = 10 XJBVD = 1
+PBS = 1 CJS = 0.0005 MJS = 0.5 PBSWS = 1
+CJSWS = 5E-010 MJSWS = 0.33 PBSWGS = 1 CJSWGS = 3E-010
+MJSWGS = 0.33 PBD = 1 CJD = 0.0005 MJD = 0.5
+PBSWD = 1 CJSWD = 5E-010 MJSWD = 0.33 PBSWGD = 1
+CJSWGD = 5E-010 MJSWGD = 0.33 TPB = 0.005 TCJ = 0.001
+TPBSW = 0.005 TCJSW = 0.001 TPBSWG = 0.005 TCJSWG = 0.001
+XTIS = 3 XTID = 3
+DMCG = 0E-006 DMCI = 0E-006 DMDG = 0E-006 DMCGT = 0E-007
+DWJ = 0.0E-008 XGW = 0E-007 XGL = 0E-008
+RSHG = 0.4 GBMIN = 1E-010 RBPB = 5 RBPD = 15
+RBPS = 15 RBDB = 15 RBSB = 15 NGCON = 1
+JTSS = 1E-4 JTSD = 1E-4 JTSSWS = 1E-10 JTSSWD = 1E-10
+JTSSWGS = 1E-7 JTSSWGD = 1E-7
+NJTS = 20.0 NJTSSW = 15 NJTSSWG = 6 VTSS = 10
+VTSD = 10 VTSSWS = 10 VTSSWD = 10
+NJTSD = 15.0 NJTSSWD = 20 NJTSSWGD = 6
+TNJTS = 0.1 TNJTSD = 0.05 +VTSSWGS=2 VTSSWGD=2
+XTSS = 0.02 XTSD = 0.02 XTSSWS = 0.02 XTSSWD = 0.02
+XTSSWGS = 0.02 XTSSWGD = 0.02
Notes: Calculate using equations, simulate to check. Then tweak.

## Slide 98: MOSFET equations for gate C in Saturation
Three components: Channel capacitance + overlap + diffusion

## Slide 99: Diode Junction Capacitance

## Slide 100: Gate Capacitance
Capacitance as a function of VGS
(with VDS = 0)
Capacitance as a function of the degree of saturation

## Slide 101: Measuring the Gate Cap
VGS(V) NMOS

## Slide 102: Varactor
va·rac·tor  vəˈraktər/
  Noun - ELECTRONICS
  A semiconductor diode with a capacitance dependent on the applied voltage.

## Slide 103: Capacitors on ICs
Question: What capacitances do you see?

## Slide 104: Miller capacitance (1/4)
Some capacitance has a perceived value larger or smaller than the physical value.
To find these capacitances, draw in the capacitance to the schematic.
Identify the end of the capacitance that is connected to the node of interest.
Identify the other side of the capacitance.
Is the other side of the capacitance moving?
If the answer is “Yes” then the perceived capacitance won’t be equal to the physical capacitance.

## Slide 105: Miller capacitance example (2/4)
Vin goes from 0 to 1
Vin node of interest
Does other side of C move?
  CGSovM2 - NO
  CGSM2 - NO
  CGDovM2 - YES
  CGBM1 - NO
  CGSovM1 - NO
  CGDovM1 - YES
M2
M1

## Slide 106: Miller capacitance example (3/4)
“Yes”s
  CGDovM2 - YES
  CGDovM1 - YES
When Vin goes from 0V to 5V
Vout goes from: 5V to 0V
Let’s see why it’s perceived as a different C
VDD
VDD

## Slide 107: Miller capacitance example (4/4)
When connected to GND:
  You move Vin VDD and the change in voltage across C is VDD
  Net voltage change across C = VDD
When other side is moving:
  You move Vin VDD and the other side moves in the opposite direction VDD
  Net voltage change across C = VDD – (-VDD) = 2VDD
VDD
VDD

## Slide 108: Miller capacitance generalized
A capacitance looks bigger by the factor:
Vin goes from 0 to VDD, Vout goes from VDD to 0:

## Slide 109: Capacitance
Diffusion
Capacitance
Diffusion
Capacitance
Channel (Gate)
Capacitance
Physical
(Overlap)
Capacitance
Physical
(Overlap)
Capacitance
Notes: Remember to explain field effect

## Slide 110: CMOS Inverter Propagation Delay Approach 1

## Slide 111: CMOS Inverter Propagation Delay Approach 1
t
pHL
= f(R
on
.C
L
)
= 0.69 R
on
C
L
V
out
V
out
R
n
R
p
V
DD
V
DD
V
in
5
V
DD
V
in
5
0
(a) Low-to-high
(b) High-to-low
C
L
C
L

## Slide 112: Question:
Is there anything wrong or missing from the previous equation and/or slide?
Didn’t take self loading into account
Didn’t take changes in capacitance into account
Didn’t take leakage into account
Didn’t take possible change in operating region into account (Assumed constant current)
Did take the pain it would cause to a human to accurately calculate the delay into account
Notes: Didn’t take self loading into account

## Slide 113: CMOS Inverter Propagation Delay Approach 2

## Slide 114: Summary of this topic
Played with regions of operation and load lines to find where graphs came from
Looked at fabrication and structure to understand where C came from (both wires and transistors)
Saw 3 ways to find Requiv of a conducting transistor
Saw how to figure out what region of operation each transistor is in right after input changes

## Slide 115: Complete example
Delay @ Vint
Vin: 0VDD
Steps:
  Figure out which node is important
    Input to second inverter
  Find R to important node
  Find C on node
  0.69 x R x C
R and C is actually distributed so not 100% accurate
NOTE:
Vin moves instantaneously
Vint is the node that you are watching so moves according to RC time constant
Vout: Assume it doesn’t move while you are calculating the delay on Vint.

## Slide 116: Example continued
First find R
Reqn = 6V / 1mA = 6KΩ
Reqp = -6V / -0.7mA = 8.57KΩ

## Slide 117: Now C (1st pass)
C on Vint
  Follow wires to all places where wire hits transistors:
    Drain of M1
    Drain of M2
    Gate of M3
    Gate of M4
  Ignore wire and Miller effect for now
NOTE:
Vin moves instantaneously
Vint is the node that you are watching so moves according to RC time constant
Vout: Assume it doesn’t move while you are calculating the delay on Vint.
M1
M4
M3
M2

## Slide 118: Now C (Add Miller)
Miller effect
  Vout doesn’t move so no Miller on M3 or M4
  Vin moves though so Miller on M1 and M2.
  Only on capacitances where both sides move:
NOTE:
Vin moves instantaneously
Vint is the node that you are watching so moves according to RC time constant
Vout: Assume it doesn’t move while you are calculating the delay on Vint.
M1
M4
M3
M2

## Slide 119: Now C (CGC)
CGC depends on region of
operation.
  Assume Vin goes from 0VDD
  Vin starts at 0 so
  Vint=VDD and Vout=0 at start.
  Vin instantaneously goes from
  0VDD.
  Vint is node of interest and starts to go from VDD0
  Vout stays at 0.
Vint=VDD so right at transition:
VGSNMOS=VDD VDSNMOS=0  Linear  CGCNMOS=CoxWL
VGSPMOS=0 VDSPMOS=VDD  Cutoff  CGCPMOS=CoxWL
NOTE:
Vin moves instantaneously
Vint is the node that you are watching so moves according to RC time constant
Vout: Assume it doesn’t move while you are calculating the delay on Vint.
M1
M4
M3
M2

## Slide 120: SPICE NMOS Model
.MODEL N1 NMOS LEVEL = 14
+VERSION = 4.6.0 BINUNIT = 1 PARAMCHK= 1 MOBMOD = 0
+CAPMOD = 2 IGCMOD = 1 IGBMOD = 1 GEOMOD = 1
+DIOMOD = 1 RDSMOD = 0 RBODYMOD= 0 RGATEMOD= 1
+PERMOD = 1 ACNQSMOD= 0 TRNQSMOD= 0 TEMPMOD = 0
+TNOM = 27 TOXE = 1.8E-009 TOXP = 10E-010 TOXM = 1.8E-009
+DTOX = 8E-10 EPSROX = 3.9 WINT = 5E-009 LINT = 1E-009
+LL = 0 WL = 0 LLN = 1 WLN = 1 +LW = 0 WW = 0 LWN = 1 WWN = 1
+LWL = 0 WWL = 0 XPART = 0 TOXREF = 1.4E-009
+SAREF = 5E-6 SBREF = 5E-6 WLOD = 2E-6 KU0 = -4E-6
+KVSAT = 0.2 KVTH0 = -2E-8 TKU0 = 0.0 LLODKU0 = 1.1
+WLODKU0 = 1.1 LLODVTH = 1.0 WLODVTH = 1.0 LKU0 = 1E-6
+WKU0 = 1E-6 PKU0 = 0.0 LKVTH0 = 1.1E-6 WKVTH0 = 1.1E-6
+PKVTH0 = 0.0 STK2 = 0.0 LODK2 = 1.0 STETA0 = 0.0 +LODETA0 = 1.0
+LAMBDA = 4E-10 VSAT = 1.1E+005 +VTL = 2.0E5 XN = 6.0 LC = 5E-9
+RNOIA = 0.577 RNOIB = 0.37 +LINTNOI = 1E-009
+TVOFF = 0.0 TVFBSDOFF = 0.0
+VTH0 = 0.25 +K1 = 0.35 K2 = 0.05 K3 = 0
+K3B = 0 W0 = 2.5E-006 DVT0 = 1.8 DVT1 = 0.52
+DVT2 = -0.032 DVT0W = 0 DVT1W = 0 DVT2W = 0
+DSUB = 2 MINV = 0.05 VOFFL = 0 DVTP0 = 1E-007
+DVTP1 = 0.05 LPE0 = 5.75E-008 LPEB = 2.3E-010 XJ = 2E-008
+NGATE = 5E+020 NDEP = 2.8E+018 NSD = 1E+020 PHIN = 0
+CDSC = 0.0002 CDSCB = 0 CDSCD = 0 CIT = 0
+VOFF = -0.15 NFACTOR = 1.2 ETA0 = 0.05 ETAB = 0
+UC = -3E-011 +VFB = -0.55 U0 = 0.032 UA = 5.0E-011 UB = 3.5E-018
+A0 = 2 AGS = 1E-020 +A1 = 0 A2 = 1 B0 = -1E-020 B1 = 0
+KETA = 0.04 DWG = 0 DWB = 0 PCLM = 0.08
+PDIBLC1 = 0.028 PDIBLC2 = 0.022 PDIBLCB = -0.005 DROUT = 0.45
+PVAG = 1E-020 DELTA = 0.01 PSCBE1 = 8.14E+008 PSCBE2 = 5E-008
+FPROUT = 0.2 PDITS = 0.2 PDITSD = 0.23 PDITSL = 2.3E+006
+RSH = 0 RDSW = 50 RSW = 50 RDW = 50
+RDSWMIN = 0 RDWMIN = 0 RSWMIN = 0 PRWG = 0
+PRWB = 6.8E-011 WR = 1 ALPHA0 = 0.074 ALPHA1 = 0.005
+BETA0 = 30 AGIDL = 0.0001 BGIDL = 2.1E+009 CGIDL =
+EGIDL = 0.8 AGISL = 0.0002 BGISL = 2.1E+009 CGISL = 0.0002
+EGISL = 0.8 +AIGBACC = 0.012 BIGBACC = 0.0028 CIGBACC = 0.002
+NIGBACC = 1 AIGBINV = 0.014 BIGBINV = 0.004 CIGBINV = 0.004
+EIGBINV = 1.1 NIGBINV = 3 AIGC = 0.012 BIGC = 0.0028
+CIGC = 0.002 AIGS = 0.012 BIGS = 0.0028 CIGS = 0.002
+NIGC = 1 POXEDGE = 1 PIGCD = 1 NTOX = 1
+AIGD = 0.01 BIGD = 0.003 CIGD = 0.0015 +XRCRG1 = 12 XRCRG2 = 5
+CGSO = 6.238E-010 CGDO = 6.238E-010 CGBO = 2.56E-011 CGDL = 2.495E-10
+CGSL = 2.495E-10 CKAPPAS = 0.03 CKAPPAD = 0.03 ACDE = 1
+MOIN = 15 NOFF = 0.9 VOFFCV = 0.02
+KT1 = -0.37 KT1L = 0.0 KT2 = -0.042 UTE = -1.5
+UA1 = 1E-009 UB1 = -3.5E-019 UC1 = 0 PRT = 0 +AT = 53000
+FNOIMOD = 1 TNOIMOD = 0
+JSS = 0.0001 JSWS = 1E-011 JSWGS = 1E-010 NJS = 1
+IJTHSFWD= 0.01 IJTHSREV= 0.001 BVS = 10 XJBVS = 1
+JSD = 0.0001 JSWD = 1E-011 JSWGD = 1E-010 NJD = 1
+IJTHDFWD= 0.01 IJTHDREV= 0.001 BVD = 10 XJBVD = 1
+PBS = 1 CJS = 0.0005 MJS = 0.5 PBSWS = 1
+CJSWS = 5E-010 MJSWS = 0.33 PBSWGS = 1 CJSWGS = 3E-010
+MJSWGS = 0.33 PBD = 1 CJD = 0.0005 MJD = 0.5
+PBSWD = 1 CJSWD = 5E-010 MJSWD = 0.33 PBSWGD = 1
+CJSWGD = 5E-010 MJSWGD = 0.33 TPB = 0.005 TCJ = 0.001
+TPBSW = 0.005 TCJSW = 0.001 TPBSWG = 0.005 TCJSWG = 0.001
+XTIS = 3 XTID = 3
+DMCG = 0E-006 DMCI = 0E-006 DMDG = 0E-006 DMCGT = 0E-007
+DWJ = 0.0E-008 XGW = 0E-007 XGL = 0E-008
+RSHG = 0.4 GBMIN = 1E-010 RBPB = 5 RBPD = 15
+RBPS = 15 RBDB = 15 RBSB = 15 NGCON = 1
+JTSS = 1E-4 JTSD = 1E-4 JTSSWS = 1E-10 JTSSWD = 1E-10
+JTSSWGS = 1E-7 JTSSWGD = 1E-7
+NJTS = 20.0 NJTSSW = 15 NJTSSWG = 6 VTSS = 10
+VTSD = 10 VTSSWS = 10 VTSSWD = 10
+NJTSD = 15.0 NJTSSWD = 20 NJTSSWGD = 6
+TNJTS = 0.1 TNJTSD = 0.05 +VTSSWGS=2 VTSSWGD=2
+XTSS = 0.02 XTSD = 0.02 XTSSWS = 0.02 XTSSWD = 0.02
+XTSSWGS = 0.02 XTSSWGD = 0.02
Notes: Calculate using equations, simulate to check. Then tweak.

## Slide 121: Cap value (left total)
Assume LD=200nm and LS=250nm and the values from the model file on the previous slide.
Transistors on left:

## Slide 123: Cap value (right total)
Assume LD=200nm and LS=250nm and the values from the model file on the previous slide. Use Tox=1.8nm.

## Slide 124: Cap value (total)
Assume LD=200nm and LS=250nm and the values from the model file on the previous slide. Use Tox=1.8nm.

## Slide 125: Delay
Vin: 0VDD
Reqn = 6V / 1mA = 6KΩ
Reqp = -6V / -0.7mA = 8.57KΩ
We’ll revisit this example including the wire after we do complex CMOS delay

## Slide 126: Metrics seen so far
DC (DC sweep)
  VIL, VIH, VOL, VOH (Voutmax, Voutmin)
  NMH=Voutmax-VIH  Noise allowed for Vin=1
  NML=VIL-Voutmin  Noise allowed for Vin=0
  Vm  Switching threshold 01 or 10 transition
Time based (Transient response)
  tpHL, tpLH, tp (From input of circuit to output of circuit)
  tr, tf (Single wire)
Undefined region
  Regenerative or not

## Slide 127: Fabrication

## Slide 128: MOSFETs in silicon (NMOS)
Silicon
P doped
N
N

## Slide 129: MOSFETs in silicon (NMOS)
Silicon
P doped
N
N
D
S
G
N
N
D
S
G

## Slide 130: MOSFETs in silicon (NMOS vs PMOS)
PMOS?
Silicon
P doped
N
N

## Slide 131: A MOSFET transistor in silicon
Side (cross-sectional) view
Top view

## Slide 132: A Modern CMOS Process
Dual-Well Trench-Isolated CMOS Process
**

## Slide 133: Modern Interconnect