## Slide 1: Sequential Logic Design

## Slide 2: Introduction to Sequential Logic
Sequential Logic: Logic that does things in sequence
Design Problem: A Counter
  Counts up to 3 Then Starts Over at 0
OK… Count up 1.
  Can’t Count up Unless You Know What Present Value… You Need Memory. You Need The Present STATE to Figure out the Next STATE. If it’s 2 now then it’ll be 3 next.
When Do You Count up?  On a Signal: Clock

## Slide 3: Clock Pulse Definition
Period
(= 1/frequency)
Positive Pulse
Positive Edge
=Rising Edge
Negative Edge
=Falling Edge
Negative Pulse
Positive Edge
=Rising Edge
Negative Edge
=Falling Edge
CLK
Clock
edge 1
Clock
edge 2
Clock
edge 4
Clock
edge 5
Clock
edge 3
Duty cycle
=% high of period

## Slide 4: Clock Pulse Definition
tf
=fall time
90%
10%
time
tr
=rise time

## Slide 6: Storing values: Flip-flops and Latches

## Slide 7: Pull-up and pull-down resistors
BIG so little current flows through it
Puts “default” value on wire
VOUT
VINA
VINB
=VINB
=VINA
=?????

## Slide 8: Pull-down resistors
BIG so little current flows through it
Puts “default” value on wire
VOUT
VINA
VINB
=VINB
=VINA
=?????
RBIG
=GND

## Slide 9: Pull-up resistors
BIG so little current flows through it
Puts “default” value on wire
VOUT
VINA
VINB
=VINB
=VINA
=?????
=VDD
R=BIG

## Slide 10: Latches and Flip-flops
Latches and flip-flops have two stable states (Saves 0 or saves 1)
You’ll hear this this called “bistable”
A latch or flip-flop stores a single bit of data
A group of N flip-flops or latches is called an N-bit register or just a register
A rising edge flip-flop can only change its value on a rising clock edge (falling edge on falling edge, dual-edge on both rising and falling edges)
A (transparent high) latch grabs the last value it sees before a falling edge and holds it until the enable signal goes high again. Input goes to output when enabled.
Flip-flops are synchronous
Latches are asynchronous when clock high

## Slide 11: Sequential Logic Components
Memory: D Flip-Flops
D Q
CLK
D Q Q+
0 0 0
0 1 0
1 0 1
1 1 1
Clock happens Here

## Slide 12: Sequential Logic Components D Flip-Flop behavior
CLK
D
Q
D Q
CLK
Clock
edge 1
Clock
edge 2
Clock
edge 4
Clock
edge 5
Clock
edge 3

## Slide 13: Flip-Flop on RT54SX-A
klabs.org/richcontent/Tutorial/MiniCourses/.../3_Sequential.ppt

## Slide 14: (Master-Slave) Flip-Flop
Master Slave

## Slide 15: (Master-Slave) Flip-Flop version 2

## Slide 16: Transistor level
Driving input node

## Slide 17: (Master-Slave) Flip-Flop version 3

## Slide 18: Design of flip-flop
Two steps:
  Look at inverter that input must drive and determine minimum Vin to that inverter that will flip its value: Vm
  Size input (pass) transistor so that it can generate Vm and switch the inverter
First find Vm on inverter.
  INV1 needs to be switched

## Slide 19: Vm
At Vm both inverters are in the active region and currents are equal:
In homework, VT, k’ and VDD are given so it’s often easier to plug in known values and then solve for Vm in terms of and .
One equation two unknowns… So need another equation… (In HW I give you W/L values)

## Slide 20: After finding Vm….
Need to drive the input to INV1 to Vm (Set the input to INV1 to Vm)
Next identify circuit that drives the input to INV1 (Next slide)

## Slide 21: The problem you are actually solving
Remove OFF transistors: Redraw:
INV1
INV1
This node drives INV1
First half of FF:
Case: D=VDD, N1=0

## Slide 22: Driving circuit
M3 starts in linear, M1 in active
Given: VDD, k’, and VT

## Slide 23: What you have
You have the voltage Vm needed to switch INV1
You have the circuit driving INV1
For the homework, M3, M4 and M5 are the same size and you pick an M1 size that makes all this work.

## Slide 24: Comments
EE306 is no design. EE307 there’s some design. EE308 there’s more. Then EE409 is all you doing design.
In this homework I give you the size of M3, M4 and M5 but in real life you’d have to pick sizes yourself. If you don’t have enough equations to find a value, you need to pick one – It’s random. If you need fast then smaller is better. For more predictability, larger. But the first sizing can be, basically, random.

## Slide 25: Analysis
WL
BL
V
DD
M
5
M
6
M
4
M
1
V
DD
V
DD
V
DD
BL
Q
=
1
Q
=
0
C
bit
C
bit

## Slide 26: Sequential Logic Components
Memory: JK Flip-Flops
J K Q+
0 0 Q-
0 1 0
1 0 1
1 1 Q-
Clock happens Here
J
K Q
CLK
J: Jam a ‘1’ in
K: Kill the value

## Slide 27: Sequential Logic Components JK Flip-Flop behavior
CLK
J
Q
K
Q
CLK
K
J
Clock
edge 1
Clock
edge 2
Clock
edge 4
Clock
edge 5
Clock
edge 3
Clock
edge 6
Clock
edge 7
Clock
edge 8

## Slide 28: Sequential Logic Components
Memory: T Flip-Flops
T Q
CLK
Clock happens Here
T Q+
0 Q-
1 Q-

## Slide 29: Sequential Logic Components Toggle Flip-Flop behavior
CLK
T
Q
T Q
CLK
Clock
edge 1
Clock
edge 2
Clock
edge 4
Clock
edge 5
Clock
edge 3

## Slide 30: Sequential Logic Components Toggle Flip-Flop behavior
CLK
T
Q
T Q
CLK
Clock
edge 1
Clock
edge 2
Clock
edge 4
Clock
edge 5
Clock
edge 3
1

## Slide 31: Sequential Logic Components
Memory: Latch
D Q
CLK
Din Clk Q+
0 0 Q (Hold)
0 1 0
0 Q (Hold)
1 1 1
Din Q
Level sensitive circuit (not edge triggered circuit)

## Slide 32: Sequential Logic Components D Flip-Flop & Latch behavior
CLK
D
Qf
Flip-flop
D Qf
CLK
Clock
edge 1
Clock
edge 2
Clock
edge 4
Clock
edge 5
Clock
edge 3
Latch
D QL
CLK
QL

## Slide 33: Master-Slave Flip-Flop Version 4
S
R
CP
S
R
S
R
Master
Slave
Y
Y’
Q
Q’
MASTER-SLAVE FLIP-FLOP
klabs.org/richcontent/Tutorial/MiniCourses/.../3_Sequential.ppt

## Slide 34: Clocked D Latch
The present state is held when CP is low.
D
CP
Q
Q’
5
3
4
1
2
klabs.org/richcontent/Tutorial/MiniCourses/.../3_Sequential.ppt

## Slide 37: Inverter sizing and generating clock signals

## Slide 38: Ring oscillators
One way to generate an on-chip clock signal (a square wave)
Other on-chip signal generation techniques may require RLC circuits and are often too slow for modern circuits.
Period
(= 1/frequency)
CLK
Clock
edge 1
Clock
edge 2
Clock
edge 4
Clock
edge 5
Clock
edge 3
Duty cycle
=% high of period

## Slide 39: Ring oscillator
Needs to be an ODD number of inverters
Simplest is three inverters:
More inverters

## Slide 40: Ring oscillator
Simplest is three inverters:
0
1
tpHL
tpLH
0
1
tpHL
1
0
tpHL
tpLH
tpLH

## Slide 41: Frequency of ring oscillator
Frequency= 1/T
Slides to add current starved

## Slide 42: Current starved ring oscillator
The speed that a node changes:
You can change tp by changing the current or capacitance but it’s hard to change capacitance
Current starved ring oscillators change the current by adding a current choking transistor

## Slide 43: Current starved ring oscillator
Example:

## Slide 44: Sequential Logic: Introduction

## Slide 45: Counter comments to here
Remember, we’re building a sequential circuit
Flip-flops hold information about present value  The value in the flip-flops is called “Present state” because it tells you where you are in the sequence
“Next state” logic take the “Present state” and calculates what the NEXT STATE will be when the clock ticks
We’ve seen two of the most important blocks

## Slide 46: Complete sequential circuit
A sequential circuit is made up of three parts:
  Present state (PS) flip-flops
  Next state (NS) logic block
  Output logic block
From here we’ll look at the process used to create a sequential circuit

## Slide 47: Sequential Logic: Design Steps and types of sequential logic

## Slide 48: Sequential Circuit Design
Steps in Designing a Sequential Circuit
UNDERSTAND PROBLEM!!!!!!!!!
Step 1:
Determine I/O
Step 2:
Decide FSM Type (Meally or Moore)
Step 4:
Draw State Transition Diagram
Step 5:
Draw Logic
Step 8:
Step 3:
Timing Diagram (To Describe & Understand Behaviour)
Write out State Transition Table
Generate Logic Equations
Step 6:
Step 7:

## Slide 49: Sequential Circuit Design
Example:
  A 2-Bit Up-Down Counter
  Step 1: Understand Problem
    A Circuit That:
      Counts UP on 1 Input (dir)
      Counts DOWN on 0 Input (dir)
      Starts at 0 After RESET Input
      Start-up Value Not Guaranteed
What’s missing?

## Slide 50: Sequential Circuit Design
Example:
  Step 2: Determine I/O
dir direction
RESET reset
clk
Q1Q0
(Count value)
2

## Slide 51: NOTE: What to draw on an IO block
IO only of complete circuit
  No input counter:
  Second design:
IO Diagram
IO Diagram

## Slide 52: Sequential Circuit Design
Example: (State = output)
  Step 3: Describe Behavior with Timing Diagram
Q1Q0 XX 00 01 10 11 00 01 00 11 10 01
State XX 00 01 10 11 00 01 00 11 10 01
CLK
Q1
Q0
RESET
dir

## Slide 53: Sequential Circuit Design
Steps in Designing a Sequential Circuit
UNDERSTAND PROBLEM!!!!!!!!!
Step 1:
Determine I/O
Step 2:
Decide FSM Type (Meally or Moore)
Step 4:
Draw State Transistion Diagram
Step 5:
Draw Logic
Step 8:
Step 3:
Timing Diagram (To Describe & Understand Behaviour)
Write out State Transition Table
Generate Logic Equations
Step 6:
Step 7:

## Slide 54: Alternate picture of Meally and Moore Machines (Maybe easier to understand)
Models: Input doesn’t go to Output Logic block for Moore
Meally Machine
(Output Depends on Input and Present State)
Output
Combinational
Logic
Output Logic
Input
CLK
Takes Present State and Produces Next State.
FF Holding
Present State
Combinational
Logic
Flip-flops
Moore Machine
(Output Depends Only on Present State)
Combinational
Logic
Output Logic
Input
CLK
Takes Present State and Produces Next State.
FF Holding
Present State
Combinational
Logic
Flip-flops

## Slide 55: Sequential Logic Models
Models: Input doesn’t go to Output Logic block for Moore
Meally Machine
Combinational
Logic
FF Holding
Present State
Output Logic
Takes Present State and Produces Next State.
Input
Output
CLK
(Output Depends on Input and Present State)
Moore Machine
Combinational
Logic
FF Holding
Present State
Output Logic
Takes Present State and Produces Next State.
Input
Output
CLK
(Output Depends Only on Present State)

## Slide 56: Sequential Logic Models
Meally Machine
  Possible Gains:
    Less Logic
    Fewer States
    Quicker Results
  Possible Dangers
    Glitching
    Feedthrough Loop
Meally Machine
(Output Depends on Input and Present State)
Output
Combinational
Logic
Output Logic
Input
CLK
Takes Present State and Produces Next State.
FF Holding
Present State
Combinational
Logic
Flip-flops

## Slide 57: Sequential Logic Models
Moore Machine
  Possible Gains:
    Robust
    Synchronized
  Possible Drawbacks
    Larger Area
Moore Machine
Combinational
Logic
FF Holding
Present State
Output Logic
Takes Present State and Produces Next State.
Input
Output
CLK
(Output Depends Only on Present State)

## Slide 58: Sequential Logic Models
Meally Machine
CLK
Input
Output
(Output Depends on Input and Present State)
Output
Combinational
Logic
Output Logic
Input
CLK
Takes Present State and Produces Next State.
FF Holding
Present State
Combinational
Logic
Flip-flops

## Slide 59: Sequential Logic Models
Moore Machine
CLK
Input
Output / D
Combinational
Logic
FF Holding
Present State
Output Logic
Takes Present State and Produces Next State.
Input
Output
CLK
(Output Depends Only on Present State)

## Slide 60: Sequential Logic Models
CLK
Input
Output / D
Moore Machine
Meally Machine
CLK
Input
Output / D

## Slide 61: Sequential Logic Models
Q3Q2Q1Q0 0000 0001 0010 0011 0100 0101 0110 01110000 0001 0010 0011…
CLK
Q3
Q2
Q1
Q0
Reset
Meally or Moore?

## Slide 62: Sequential Circuit Design
Example:
  Step 4: Select Model Type. Meally or Moore?
CLK
Q1
Q0
Q1Q0 XX 00 01 10 11 00 01 00 11 10 01
RESET
dir
Moore

## Slide 63: Sequential Circuit Design
Example:
  Step 4: Select Model Type. Meally or Moore?
CLK
Q1
Q0
Q1Q0 XX 00 01 10 11 00 01 00 11 10 01
RESET
dir
Meally

## Slide 64: Sequential Logic Models
CLK
Q3
Q2
Q1
Q0
Q3Q2Q1Q0 0000 0001 0010 0011 0100 0101 0110 0111 1000 1001 1010 1011…
Meally or Moore?

## Slide 65: Sequential Logic Design
Steps in Designing a Sequential Circuit
UNDERSTAND PROBLEM!!!!!!!!!
Step 1:
Determine I/O
Step 2:
Decide FSM Type (Meally or Moore)
Step 4:
Draw State Transistion Diagram
Step 5:
Draw Logic
Step 8:
Step 3:
Timing Diagram (To Describe & Understand Behaviour)
Write out State Transition Table
Generate Logic Equations
Step 6:
Step 7:

## Slide 66: State Transition Diagrams
Different for Meally & Moore Models
Meally
Moore
State Name
State Value
[Input/Output Value]
Next State
State Name
State Value
[Output Value]
Next State
[Input Value]

## Slide 67: Selecting State Bubble Stuff (1)
State name: Something descriptive of the state’s function. Words are good. For humans.
  ie “Add numbers”
State Value: Each state must have a numerical name. It must be unique (different from all other state values in the machine). For computer.
  ie For a four-state machine: 00, 01, 10, 11.
  ie For a five state machine: 000, 001, 010, 011, 100, 101
  ie For a four state machine: 0000, 1001, 1010, 1011, 1100

## Slide 68: Selecting State Bubble Stuff (2)
Output value: A list of ‘1’s and ‘0’s corresponding to the outputs of the state machine.
  ie [1011] for a state machine with outputs [Enable, Add, Subtract, SaveResult]
Input value: A list of ‘1’s and ‘0’s corresponding to the inputs of the state machine (often come from blocks the FSM controls).
  ie [010] for a state machine with outputs [ResetAll, MultiplyDone, Negative?]

## Slide 69: Selecting State Bubble Stuff (3)
Legend/Key – for input and output
  You can write inputs and outputs as 0s and 1s OR you can write the names of the signals. For example the counter’s outputs were: OP1 and OP0
  The output can be written: 10 or
  Non-negated means ‘1’ and negated means ‘0’
BUT: If you write ‘10’, you need to tell me what that means. You need a legend. Here’s an example (on next slide)

## Slide 70: Sequential Circuit Design
State name: Zero, One
State value: 00, 01
Zero
00
[010]
One
01
[111]
0000
0001
0101
1100
1011
1101
• • •
• • •
Key: Input: Button1, Button2, DoorOpen, KeyTurned
Output: StartCar, TurnOnStartLight, LockDoors

## Slide 71: Sequential Circuit Design
Example:
  Step 5: Draw the State Transition Diagram
Zero
00
[0]
One
01
[1]
Two
11
[2]
Three
10
[3]
0
0
0
0
1
1
1
1
RESET
RESET
RESET
RESET
RESET

## Slide 72: Sequential Circuit Design
Example:
  Step 5: Draw the State Transition Diagram
Zero
00
[00]
One
01
[01]
Two
11
[10]
Three
10
[11]
0
0
0
0
1
1
1
1
RESET
RESET
RESET
RESET
RESET

## Slide 73: Sequential Circuit Design
Example:
  Step 6: Draw the State Transition Table
Output Logic
Present State
Output
2
2
Next
State
Logic
Present State
direction
Next State
RESET
2
2
Output Logic
Next State Logic

## Slide 74: Sequential Circuit Design
Example:
  Step 6: Draw the State Transition Table
Output Logic
Present State
Output
P1 P0 O1 O0
0 0 0 0
0 1 0 1
1 0 1 1
1 1 1 0
Zero
00
[0]
One
01
[1]
Two
11
[2]
Three
10
[3]
0
0
0
0
1
1
1
1
2
2
RESET

## Slide 75: Sequential Circuit Design
Example:
  Step 6: Draw the State Transition Table
rst P1 P0 dir N1 N0
0 0 0 0 1 0
0 0 0 1 0 1
0 0 1 0 0 0
0 0 1 1 1 1
0 1 0 0 1 1
0 1 0 1 0 0
0 1 1 0 0 1
0 1 1 1 1 0
1 X X X 0 0
Zero
00
[00]
One
01
[01]
Two
11
[10]
Three
10
[11]
0
0
0
0
1
1
1
1
RESET
Next
State
Logic
Present State
direction (dir)
Next State
RESET (rst)
2
2
NOTE: This truth table won’t be acceptable in this class unless I say so in question

## Slide 76: Sequential Circuit Design
Example:
  Step 7: Derive Logic
    Output
      O1=P1
      O0=P1P0
    Next State
      N1=(P1dir)•rst
      N0=(P1dir)•rst
P1 P0 O1 O0
0 0 0 0
0 1 0 1
1 0 1 1
1 1 1 0
rst P1 P0 dir N1 N0
0 0 0 0 1 0
0 0 0 1 0 1
0 0 1 0 0 0
0 0 1 1 1 1
0 1 0 0 1 1
0 1 0 1 0 0
0 1 1 0 0 1
0 1 1 1 1 0
1 X X X 0 0

## Slide 77: Sequential Circuit Design
Example:
  Step 8: Draw Logic
    O1=P1
    O0=P1P0
    N1=P1IN
    N0=P1IN
Moore Machine
FF
O1=P1
O0=P1P0
N1=P1IN
N0=P1IN
Input
Output
CLK
2
2
2
2

## Slide 78: Sequential Logic Design
Steps in Designing a Sequential Circuit
UNDERSTAND PROBLEM!!!!!!!!!
Step 1:
Determine I/O
Step 2:
Decide FSM Type (Meally or Moore)
Step 4:
Draw State Transistion Diagram
Step 5:
Draw Logic
Step 8:
Step 3:
Timing Diagram (To Describe & Understand Behaviour)
Write out State Transition Table
Generate Logic Equations
Step 6:
Step 7:

## Slide 79: State Transition Diagrams
Same Example Except Use Meally Model:
Step 1Thru 2 are the Same
  Step 3: Describe Behavior with Timing Diagram
  Step 4: Meally or Moore?
  Meally
CLK
Q1
Q0
Q1Q0 XX 00 01 10 11 00 01 10 11 00 01
Reset

## Slide 80: State Transition Diagrams
Different for Meally & Moore Models
Meally
Moore
State Name
State Value
[Input/Output Value]
Next State
State Name
State Value
[Output Value]
Next State
[Input Value]

## Slide 81: Sequential Circuit Design Non-Mealy Mealy, No need for Mealy
Example:
  Step 5: Draw the State Transition Diagram
Zero
00
One
01
Two
11
Three
10
0/10
0/01
0/00
0
1
1
1
1
RESET/00
Doesn’t work
RESET
RESET/10
RESET/11
RESET/00
/00
/01
/10
/11
/01
/11

## Slide 82: Sequential Circuit Design
Example:
  Step 5: Draw the State Transition Diagram
Zero
00
One
01
Two
11
Three
10
0/01
0/00
0/11
0
1
1
1
1
RESET/00
RESET
RESET/00
RESET/00
RESET/00
/01
/10
/11
/00
/00
/10

## Slide 83: Sequential Circuit Design
Same Example Except Use Meally Model :
  Step 5: Draw the State Transition Diagram
Zero
00
One
01
Two
11
Three
10
0/01
0/00
0/11
0/10
1/10
1/01
1/00
1/11
RESET/00

## Slide 84: Sequential Circuit Design
Same Example Except Use Meally Model :
  Step 6: Draw the State Transition Table
Next
State
Logic
Present State
direction
Next State
RESET
2
2
Output Logic
Present State
Output
direction
RESET
2
2
Output Logic
Next State Logic

## Slide 85: Sequential Circuit Design
Same Example Except Use Meally Model :
  Step 6: Draw the State Transition Table
Zero
00
One
01
Two
11
Three
10
0/01
0/00
0/11
0/10
1/10
1/01
1/00
1/11
Output Logic
Present State
Output
direction
RESET
2
2
rst P1 P0 dir O1 O0
0 0 0 0 1 1
0 0 0 1 0 1
0 0 1 0 0 0
0 0 1 1 1 0
0 1 0 0 1 0
0 1 0 1 0 0
0 1 1 0 0 1
0 1 1 1 1 1
1 X X X 0 0

## Slide 86: Sequential Circuit Design
Same Example Except Use Meally Model :
  Step 6: Draw the State Transition Table
Zero
00
One
01
Two
11
Three
10
0/01
0/00
0/11
0/10
1/10
1/01
1/00
1/11
rst P1 P0 dir N1 N0
0 0 0 0 1 0
0 0 0 1 0 1
0 0 1 0 0 0
0 0 1 1 1 1
0 1 0 0 1 1
0 1 0 1 0 0
0 1 1 0 0 1
0 1 1 1 1 0
1 X X X 0 0
Next
State
Logic
Present State
direction
Next State
RESET
2
2

## Slide 87: Sequential Circuit Design
Example:
  Step 7: Derive Logic
    Output
      O1=(P0dir)•rst
      O0=(P1P0)•rst
    Next State
      N1=(P0dir)•rst
      N0=(dirP1)•rst
rst P1 P0 dir O1 O0
0 0 0 0 1 1
0 0 0 1 0 1
0 0 1 0 0 0
0 0 1 1 1 0
0 1 0 0 1 0
0 1 0 1 0 0
0 1 1 0 0 1
0 1 1 1 1 1
1 X X X 0 0
rst P1 P0 dir N1 N0
0 0 0 0 1 0
0 0 0 1 0 1
0 0 1 0 0 0
0 0 1 1 1 1
0 1 0 0 1 1
0 1 0 1 0 0
0 1 1 0 0 1
0 1 1 1 1 0
1 X X X 0 0

## Slide 88: Sequential Circuit Design
Example:
  Step 8: Draw Logic
    Output
      O1=(P0dir)•rst
      O0=(P1P0)•rst
    Next State
      N1=(P0dir)•rst
      N0=(dirP1)•rst
Meally Machine
Combinational
Logic
FF Holding
Present State
O1=(P0dir)•rst
O0=(P1P0)•rst
N1=(P0dir)•rst
N0=(dirP1)•rst
Input
Output
CLK

## Slide 89: Class Problem: Digital Debouncer
Push-button switches, toggle switches, and electro-mechanical relays bounce:
Let’s say you know that the maximum time a switch can bounce is 1μs+ (a bit more than 1μs) and your clock is at 3MHz. Build (separately) a Meally and a Moore machine that tells you when you’ve stopped bouncing and have gone from 0 to 1.

## Slide 90: Sequential Logic Design
Steps in Designing a Sequential Circuit
UNDERSTAND PROBLEM!!!!!!!!!
Step 1:
Determine I/O
Step 2:
Decide FSM Type (Meally or Moore)
Step 4:
Draw State Transistion Diagram
Step 5:
Draw Logic
Step 8:
Step 3:
Timing Diagram (To Describe & Understand Behaviour)
Write out State Transition Table
Generate Logic Equations
Step 6:
Step 7:

## Slide 91: Sequential Logic: Examples

## Slide 92: My Specifications (Digital Debouncer)
If 4 clock cycles after I see a ‘1’, I see a ‘1’, again then I will assume that the input has switched from 01 and I should output a 1.
Whenever I am in the “found a 1” state and I see a 0, I will switch to the wait state.

## Slide 93: Determine I/O (Digital Debouncer)
Button
Output
clk
Cleaned
Button
Output

## Slide 94: Timing Diagram (Digital Debouncer)
Moore Machine
Input
Combinational
Logic
FF Holding
Present State
Output Logic
Takes Present State and Produces Next State.
Output
CLK
D Q
CLK
CLK
Input
Output

## Slide 95: State Transition Diagram (Digital Debouncer)
Wait/Low
000
[0]
Sensed 1
001
[0]
Sensed 3
011
[0]
Three
101
[1]
0
X
X
1
0
1
Sensed 2
010
[0]
X
Sensed 4
100
[0]
1
0

## Slide 96: Output Logic (Digital Debouncer)
Output Logic
Present State
Output
P2 P1 P0 Out
0 0 0 0
0 0 1 0
0 1 0 0
0 1 1 0
1 0 0 0
1 0 1 1
1 1 0 X
1 1 1 X
Out=P2•P1•P0
3

## Slide 97: Next State Logic (Digital Debouncer)
In P2 P1 P0 NS2 NS1 NS0
0 0 0 0 0 0 0
0 0 0 1 0 1 0
0 0 1 0 0 1 1
0 0 1 1 1 0 0
0 1 0 0 1 0 1
0 1 0 1 0 0 0
0 1 1 0 X X X
0 1 1 1 X X X
1 0 0 0 0 0 1
1 0 0 1 0 1 0
1 0 1 0 0 1 1
1 0 1 1 1 0 0
1 1 0 0 1 0 1
1 1 0 1 1 0 1
1 1 1 0 X X X
1 1 1 1 X X X
I’ll let you do the logic
Next State Logic
Present State
Output
3
Button Input

## Slide 98: Meally version: My Specifications (Digital Debouncer)
If 4 clock cycles after I see a ‘1’, I see a ‘1’, again then I will assume that the input has switched from 01 and I should output a 1.
Whenever I am in the “found a 1” state and I see a 0, I will switch to the wait state.

## Slide 99: Determine I/O (Digital Debouncer)
Button
Output
clk
Cleaned
Button
Output

## Slide 100: Timing Diagram (Digital Debouncer)
Meally Machine
D Q
CLK
CLK
Input
Output
Combinational
Logic
FF Holding
Present State
Output Logic
Takes Present State and Produces Next State.
Input
Output
CLK

## Slide 101: State Transition Diagram (Digital Debouncer)
Wait/Low
000
Sensed 1
001
Sensed 3
011
0/0
1/0
Sensed 2
010
X/0
Sensed 4
100
X/0
X/0
0/0
1/1

## Slide 102: Output Logic (Digital Debouncer)
Output Logic
Present State
Output
3
In P2 P1 P0 Out
0 0 0 0 0
0 0 0 1 0
0 0 1 0 0
0 0 1 1 0
0 1 0 0 0
0 1 0 1 X
0 1 1 0 X
0 1 1 1 X
1 0 0 0 0
1 0 0 1 0
1 0 1 0 0
1 0 1 1 0
1 1 0 0 1
1 1 0 1 X
1 1 1 0 X
1 1 1 1 X
By examination:
Out=In•P2

## Slide 103: Next State Logic (Digital Debouncer)
I’ll let you do the logic
Next State Logic
Present State
Output
3
Button Input
In P2 P1 P0 NS2 NS1 NS0
0 0 0 0 0 0 0
0 0 0 1 0 1 0
0 0 1 0 0 1 1
0 0 1 1 1 0 0
0 1 0 0 0 0 0
0 1 0 1 X X X
0 1 1 0 X X X
0 1 1 1 X X X
1 0 0 0 0 0 1
1 0 0 1 0 1 0
1 0 1 0 0 1 1
1 0 1 1 1 0 0
1 1 0 0 1 0 0
1 1 0 1 X X X
1 1 1 0 X X X
1 1 1 1 X X X

## Slide 104: Today…
Meally to logic
One-hot encoding

## Slide 105: Class Problem
Pattern Finder
  Build a circuit that takes a bit stream in and gives a single high pulse, one clock cycle long, when the pattern has been found. The pattern is: 0010. No overlapping allowed. For example, 00100010 counts as two sequences but 0010010 does not count as two patterns.

## Slide 106: Terms
FSM: A sequential circuit with a finite number of states…
Sequential circuit/logic: A circuit that does things in a specific order
Register: A group of flip-flops

## Slide 107: Sequential Logic: Cooperating FSMs

## Slide 108: Cooperating FSMs
Simple definition: A system made up of more than one FSM where the system’s FSMs talk to each other and give each other information about what they are doing
Example 1: A computer
  Instruction: C=A+B
  Main FSM to memory FSM: Get ‘A’ for me
  Memory FSM to Main FSM: ‘A’ ready at my output
  Main FSM to memory FSM: Get ‘B’ for me
  Memory FSM to Main FSM: ‘B’ ready at my output
  Main FSM to datapath: Add ‘A’ and ‘B’
  Main FSM to memory FSM: Store result in ‘C’ for me

## Slide 109: Cooperating FSMs
Example 2: A doorbell that plays music. The doorbell is pushed. An FSM finds the rising edge of the button being pushed (see debouncing circuit example). When it finds an edge it tells another FSM that plays a song to start. The doorbell FSM turns off until music FSM says it’s done.

## Slide 110: Cooperating FSMs
Another important use for cooperating FSMs is to reduce debugging and simplify design
As the number of states increases in a FSM, debugging becomes exponentially more difficult
Large FSMs can be divided into smaller FSMs
Here’s an example:

## Slide 111: Cooperating FSM from one large FSM
Wait/Low
000
[0]
Sensed 1
001
[0]
Sensed 3
011
[0]
Three
101
[1]
0
X
0
1
0
1
Sensed 2
010
[0]
1
Sensed 4
100
[0]
1
0
0
1
0

## Slide 112: Cooperating FSM from one large FSM
Wait/Low
000
[0]
Sensed 1
001
[0]
Sensed 3
011
[0]
Three
101
[1]
0
X
0
1
0
1
Sensed 2
010
[0]
1
Sensed 4
100
[0]
1
0
0
1
0

## Slide 113: Cooperating FSM from one large FSM
Sensed 3
011
[0]
Sensed 1
001
[0]
X
0
Sensed 2
010
[0]
1
0
1
Wait/Low
000
[0]
Three
101
[1]
0
1
0
1
Sensed 4
100
[0]
1
0
0

## Slide 114: Cooperating FSM from one large FSM
Wait/Low
000
[01]
Three
101
[10]
0XXX
1XXX
0XXX
1XXX
Sensed 4
100
[00]
1XXX
0XXX
0XXX
KeyA: Input: IN, To_FSMA1, To_FSMA2, To_FSMA3
Output: OUT, To_FSMB
KeyB: Input: IN, To_FSMB
Output: OUT, To_FSMA1 , To_FSMA2
To_FSMA3
FSMA
FSMB
WAIT_A
110
[00]
11XX
Sensed 3
011
[0010]
Sensed 1
001
[0001]
XX
0X
Sensed 2
010
[0100]
1X
0
1X
WAIT_A
110
[0000]
11
X0
X000
XX1X
0XX1

## Slide 115: Cooperating FSMs practice
A doorbell that has two FSMs
  The edge detector to detect when the doorbell was pushed
  An FSM that plays a song when the doorbell is pushed
  The song is not interrupted when the doorbell is pushed while song is playing – button is ignored
  Details on next slides. This could be a description that your boss brings you.

## Slide 116
Rules:
In this system, a low voltage means a logic 0 and a high voltage means a logic 1.
Before the doorbell is pushed there is a high signal on the wire to your FSM.
While the doorbell is pushed the signal to your FSM is low.
Your FSM watches the signal from the doorbell and when the doorbell is pushed (when the signal from the doorbell goes from high to low) sends a signal to a music player – a single high pulse. Let’s call this the START signal.

## Slide 117
Rules:
The music player plays and when it has finished its song sends a DONE signal (asserted high – it’s low and then goes high when it is done) back to your sequential circuit – again a single high pulse.
Your FSM is not allowed to send another START signal until it receives a DONE signal from the music player.
After receiving a done signal it should go back to waiting for another doorbell push.
A detail: Note that if the person at the doorbell pushes it and holds it until the song finishes, the song should not start again. As described in RULE iv), the must go from the released state to the pushed state for the song to be started.

## Slide 118: Timing diagram
CLK |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
IN |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
DONE |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
START |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
CLK |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
IN |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
DONE |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
START |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 119: Sequential Logic: One-hot encoding

## Slide 120: Comment On State Value
We’ve assigned state values such that we use the minimum number of flip-flops (possibly saving area and power but not guaranteed).
There are methods to assign state values such that logic transitions a minimum number of times (saving power) but we’ll leave that to those of you interested in CAD.
A method which saves logic at the expense of using many flip-flops is called “one-hot encoding”

## Slide 121: One-hot Encoding
One-hot encoding assignment rules:
  There are at least as many digits as states in state value.
  All digits except one are zero.
(Ex: 000100, 100000 could be two state values of a six-state machine)
Common minimum flip-flop state value assignment for four state FSM:
  00, 01, 10, 11
Common one-hot encoded state value assignment for four state FSM:
  0001, 0010, 0100, 1000

## Slide 122: Why One-hot Encoding?
Typically faster. Highly encoded machines get slower as more states are added. Transitions only depend on transitions into state.
Easy to design. In gates and HDL.
Modifications are straight forward.
Debugging is straight forward.
Critical path easy to find.
Usually FF extra resource on FPGAs. Area cost usually acceptable for other implementations.

## Slide 123: AND…
You don’t need to make a truth table to find logic
When do you NOT want to use a truth table?

## Slide 124: Example
Zero
00
[00]
One
01
[01]
Two
11
[10]
Three
10
[11]
0
0
0
0
1
1
1
1
rst P1 P0 dir N1 N0
0 0 0 0 1 0
0 0 0 1 0 1
0 0 1 0 0 0
0 0 1 1 1 1
0 1 0 0 1 1
0 1 0 1 0 0
0 1 1 0 0 1
0 1 1 1 1 0
1 X X X 0 0
Next
State
Logic
Present State
direction (dir)
Next State
RESET (rst)
2
Zero
0001
[10]
One
0010
[11]
Two
0100
[10]
Three
1000
[11]
0
0
0
0
1
1
1
1
rst P3P2P1P0 dir N3N2N1N0 O1O0
0 0 0 0 1 0 1 0 0 0 0 0
0 0 0 1 0 0 0 0 0 1 0 1
0 0 1 0 0 0 0 0 1 0 1 0
0 1 0 0 0 0 0 1 0 0 1 1
0 0 0 0 1 1 0 0 1 0 0 0
0 0 0 1 0 1 0 1 0 0 0 1
0 0 1 0 0 1 1 0 0 0 1 0
0 1 0 0 0 1 0 0 0 1 1 1
1 X X X X 0 0 0 0 1 State
OP Value

## Slide 125: One-Hot Encoding Logic
Resulting logic (By examination)
NS3 = (P0•Dir + P2•Dir) •Reset
NS2 = (P3•Dir + P1•Dir) •Reset
NS1 = (P2•Dir + P0•Dir) •Reset
NS0 = (P1•Dir + P3•Dir) + Reset
O1 = P2 + P3
O0 = P1 + P3
You don’t need truth tables!!!!
STD to logic
Zero
0001
[00]
One
0010
[01]
Two
0100
[10]
Three
1000
[11]
0
0
0
0
1
1
1
1
RESET

## Slide 126: One-Hot Encoding Logic
Resulting logic (By examination)
NS3 = (P0•Dir + P2•Dir)
NS2 = (P3•Dir + P1•Dir)
NS1 = (P2•Dir + P0•Dir)
NS0 = (P1•Dir + P3•Dir)
O1 = P2 + P3
O0 = P1 + P3
You don’t need truth tables!!!!
STD to logic
Zero
0001
[00]
One
0010
[01]
Two
0100
[10]
Three
1000
[11]
0
0
0
0
1
1
1
1
RESET

## Slide 127: Class Question: One-Hot Encoding
Find the logic equations for output and next state by inspection. Input = IN, output=X, Y
Zero
0001
[00]
One
0010
[01]
Two
0100
[01]
Three
1000
[10]
0
0
0
0
1
1
1
1

## Slide 128: Class Question: One-Hot Encoding
Find the logic equations for output and next state by inspection. Input = IN, output=X, Y
Zero
0001
[00]
One
0010
[01]
Two
0100
[01]
Three
1000
[10]
0
0
0X
0
1
1
1X
1

## Slide 129: Sequential Logic: Jump counter designs – Thurs, 12-2 (Review)

## Slide 130: Jump-Counter FSM Design
If a state machine basically just counts up, a counter can be used as the next state logic. The next state logic circuit for this STD is:
Zero
00
[0]
One
01
[1]
Two
10
[2]
Three
11
[3]
0
1
Load
Reset
D count
CLK
10
Dir
S1
S0
On Start-up

## Slide 131: Class Question: Jump-Counter FSM Design
Assign state values and design next state logic circuit.
Zero
[0]
One
[1]
Two
[2]
Three
[3]
0
1

## Slide 132: Sequential Logic: Microcontrollers and microprocessors

## Slide 133: Microcontroller / Microprocessor
If something is sequential, might as well write a program to do it if:
  Don’t care about substrate cost
  Don’t care about fine tuning the timing
  You are a CE or CS major
  Don’t care about wasting power

## Slide 134: MICRO-CONTROLLER
Instead of a FSM, a microcontroller runs its own program that does the same thing as a FSM
Sequential processing
Can be used to interpret another program

## Slide 135: Summary of sequential and combinational design methods

## Slide 136: Review of Combinational Logic Generation
Method | Good | Bad
TTLogic |  | 
TTKmapLogic |  | 
TTROM |  | 
TTLogicDecoder |  | 
Cascaded Logic |  | 

## Slide 137: Review of Sequential Logic Generation
Method | Good | Bad
STDSTTLogic | Mechanical-easy Easier to change than Kmap | Lotta gates Not good for a lot of Ips
STDSTTKmapLogic | Saves gates Can find glitches | Not as clear what logic does Harder to change
STDOne-Hot Encoding | Easy Can do a lot of Ips Simple | Wastes bits/Flip flops
Cooperating FSMs | Truly easier to debug Modularity | For large STDs
Micro-controller | Just write a program | Waste Slower
Jump-Counter | Good for sequential, single arrow out of state, sequential circuits… | 

## Slide 138: Logic generation
Gate level / Logic level design for
  Minimum area
  Maximum speed
  Minimum power
Transistor level
  Type of logic family for each
No software so that’s all we can do for now

## Slide 139: Flip-flop timing issues

## Slide 140: Digital circuit most common pattern
Flip-flop  Logic  Flip-flop
Meally Machine
(Output Depends on Input and Present State)
Output
Combinational
Logic
Output Logic
Input
CLK
Takes Present State and Produces Next State.
FF Holding
Present State
Combinational
Logic
Flip-flops
Moore Machine
(Output Depends Only on Present State)
Combinational
Logic
Output Logic
Input
CLK
Takes Present State and Produces Next State.
FF Holding
Present State
Combinational
Logic
Flip-flops

## Slide 141: Flip-Flop Parameters
Calculating Delay
  tclkQ  Time From Clock Tick to Q Changing
  tsetup  Time Before Clock Tick that Input (D) Can’t Change (Value Must be Stable)
  thold  Time After Clock Tick that Input (D) Can’t Change (Value Must be Stable)
D Q
CLK
Clk
D
Q
tclkQ
thold
tsetup

## Slide 142: Flip-Flop Parameters
(http://www.onsemi.com/pub/Collateral/NL17SZ74-D.PDF)

## Slide 143: Flip-Flop Parameters

## Slide 144: Flip-Flop Parameters Hold Time Failure
Why are these values important?
  What happens when TclkQ is fast and there is a long hold time?
D1 Q1
CLK
D2 Q2
CLK
tclkQ
thold
tsetup
Clk
D1
Q1=D2
Q2

## Slide 145: Flip-Flop Parameters Hold Time Success
Why are these values important?
  What happens when TclkQ is slow and there is a short hold time?
D1 Q1
CLK
D2 Q2
CLK
tsetup
tclkQ
thold
Clk
D1
Q1=D2
Q2

## Slide 146: Flip-Flop Parameters - Setup Time Failure
Why are these values important?
  What happens when TclkQ is very slow and there is a long setup time?
D1 Q1
CLK
D2 Q2
CLK
Clk
D1
Q1=D2
Q2
tclkQ
thold
tclkQ
thold
tsetup
tsetup

## Slide 147: Flip-Flop Parameters Setup Time Success
Why are these values important?
  What happens when TclkQ is slow and there is a short hold time?
D1 Q1
CLK
D2 Q2
CLK
Clk
D1
Q1=D2
Q2
tclkQ
thold
tclkQ
thold
tsetup
tsetup

## Slide 148: Example problem
Draw the timing diagram for the following cases. Tell me if there is a hold-time or setup-time violation or if they will work just as they are. If a violation occurs, identify the flip-flop where it occurs and what violation it is.
  What happens if there is no delay (Delay = 0ns)?
  What happens if there’s a 15ns period and delay=3ns?
  What happens if there’s a 15ns period and delay=9ns?

## Slide 149: Substrates

## Slide 150: Substrates
FPGA
FPAA
Breadboard
PCB (Printed circuit board)
PAL (POS), PLA (SOP)
ASIC, Custom
When is each good?